Section Cover Page

Section 08 11 69 2008-05-01 Aluminum Storm Doors

Use this Section to specify requirements for prepackaged, modular-sized combination storm/screen doors, including door, frame components, hardware, weatherstripping and thresholds, for attachment to entrance door frames.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Data Sheet – Reference Documents

.3	Specification Section Text:

1.	General

1.1	Related Sections

1.2	Reference Documents

1.3	Description of Doors

1.4	Submittals

2.	Products

2.1	General

2.2	Materials

2.3	Hardware

2.4	Fabrication

2.5	Finishes

3.	Execution

3.1	Installation

Applicable Standards:

.1	CAN/CGSB-12.1-M90	Tempered or Laminated Safety Glass

.2	CAN/CGSB 79.1-M91	Insect Screens

.3	CGSB 82-GP-3M 	Doors, Aluminum, Combination Storm and Screen.

END OF DATA SHEET

1.	General

1.1	RELATED SECTIONS

.1	Packaged, Insulated Steel Door Assemblies:	Section 08 13 90.

1.2	REFERENCE DOCUMENTS

.1	Meet or exceed requirements of CGSB 82-GP-3M, Doors, Aluminum, Combination Storm and Screen.

1.3	DESCRIPTION OF DOORS

.1	Provide assemblies consisting of the following:

.1	Door components, including:

.1	Stiles and rails.

.2	Fixed and operable glass panels.

.3	Fixed screen.

.4	Bottom kick panel.

.2	Door frame components.

.3	Hardware, including:

.1	Latchset and hinges.

.2	Door closer.

.3	Safety door check.

.4	Weather-stripping, including sweep.

.4	Accessories.

1.4	SUBMITTALS

.1	Comply with requirements of Division 01.

.2	Provide data indicating door construction, hardware, corner reinforcement, method of glazing, installation tolerances, and door elevation.

2.	Products

2.1	GENERAL

.1	Door classification to CGSB 82-GP-3M as follows:

.1	Type 1 - Self-storing Glass and Screen Inserts.

.2	Class A - Extruded Aluminum.

2.2	MATERIALS

.1	Glass:  clear, tempered safety glass to CAN/CGSB-12.1-M90.

.2	Insect Screen:  size to suit operable glass panel and to CAN/CGSB 79.1-M91 as follows:

.1	Type 2 - Heavy Duty.

.2	Class C - Fixed.

.3	Style 1 - Aluminum Screening.

2.3	HARDWARE

.1	Provide hardware to CGSB 82-GP-3M.

.2	Closer shall include integral hold-open device.

2.4	FABRICATION

.1	Glazing Arrangement:  [full width fixed and vertical sliding glass panels] [vertical sliding glass panel centred between fixed glass panels].

SPEC NOTE:  Coordinate with door elevations on drawings.

.2	Size doors to fit into designated door frames.

.3	Assemble stiles and rails with hairline corner joints, aligned and secured with corner reinforcement.

2.5	FINISHES

.1	Exposed Aluminum Surfaces:  [mill finish] [white baked enamel] [brown baked enamel] [        ].

3.	Execution

3.1	INSTALLATION

.1	Install door assemblies where indicated [on schedules] [on drawings], in accordance with manufacturer's instructions.

.2	Accurately fit and secure door frame to door opening.  Adjust door and hardware for smooth operation.

.3	Install weather-stripping for continuous seal.

END OF SECTION