Section Cover Page

Section 22 11 20 Cleaning 2010-12-01 Domestic Water Systems

Use this Section to specify the cleaning of domestic water systems.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Intent

1.2	Submittals

2.	Products

Not Used

3.	Execution

3.1	Cleaning - General

3.2	Cleaning Procedure

1.	General

1.1	INTENT

.1	This Section specifies services and material required for onsite, cleaning of a hot and cold domestic water system.

1.2	SUBMITTALS

.1	Submit a written report of actual cleaning activities including:

.1	Times.

.2	System status.

.3	Problems encountered.

.4	Actions taken.

.5	Inspection results.

2.	Products

NOT USED

3.	Execution

3.1	CLEANING - GENERAL

.1	Maintain following conditions during cleaning process:

.1	Manual and automatic valves are in full open position.

.2	By-pass valves are operated to ensure full flow through entire system.

.3	Safety devices, including pressure relief valves are functioning.

.4	System is operated with a minimum pressure of 35 kPa(g) at highest point.

3.2	CLEANING PROCEDURE

.1	Flush system to remove loose debris and solder slag.

END OF SECTION