Section Cover Page

Section 22 42 00 2008-05-01 Plumbing Fixtures and Trim

This Master Specification Section contains:

.1	This Cover Page

.2	Data  Sheet – Reference Documents

.3	Specification Section Text:

1.	General

1.1	Related Sections

1.2	Products Options and Substitutions

1.3	Quality Assurance

1.4	Coordination

2.	Products

2.1	Fixture Brass and Accessories

2.2	Water Closet

2.3	Water Closet - Water Efficient

2.4	Urinal

2.5	Urinal - Water Efficient

2.6	Lavatories

2.7	Barrier-Free Lavatories

2.8	Shampoo Sink

2.9	Stainless Steel Sinks

2.10	Bathtub [and Shower]

2.11	Shower Cabinet

2.12	Service or Mop Sinks

3.	Execution

3.1	Installation

3.2	Fixtures Rough-In Schedule

Applicable Standards:

1.	CAN/CSA-B45 Series-94	Plumbing Fixtures (Including Standards on Fixtures for Use in Recreational Vehicles)

END OF DATA SHEET

1.	General

1.1	RELATED SECTIONS

SPEC NOTE:  Include this article when a Bathing and Patient Lift System has been specified in Section 11 73 00.

.1	Bathing and Patient Lift System	Section 11 73 00

1.2	PRODUCT OPTIONS AND SUBSTITUTIONS

.1	Refer to Division 01 for requirements pertaining to product options and substitutions.

1.3	QUALITY ASSURANCE

.1	Plumbing fixtures shall meet or exceed CAN/CSA-B45 Series, CSA Standards on Plumbing Fixtures and shall be approved by the authority having jurisdiction.

.2	Plumbing fixtures shall be tested, certified and labeled in accordance with the CSA, Warnock Hersey, or other certification program accredited by the Standards Council of Canada.

.3	Each of the following products shall be by a single manufacturer:

.1	Fixtures of the same type or group.

.2	Fittings of the same type.

1.4	COORDINATION

.1	Check millwork shop drawings.  Confirm location and size of fixtures and openings before rough-in and installation.

2.	Products

2.1	FIXTURE BRASS AND ACCESSORIES

.1	Visible parts of fixture brass and accessories shall be chrome plated.

SPEC NOTE:  Review with the Lodge Foundation prior to selection of the fixture and the height of water closet required.

2.2	WATER CLOSET

.1	Bowl:  Floor-mounted, siphon jet, close-coupled closet with elongated rim and [insulated] [regular] tank, flapper type flush valve, [Crane Hymont 3-155, combination] [Crane, combination] [            ].

.2	Seat:  Solid white plastic, open front, extended back, less cover, complete with self-sustaining hinge, [Olsonite #10 SS] [            ].

2.3	WATER CLOSET - WATER EFFICIENT

.1	Bowl:  [Front] [Reverse trap] close-coupled closet combination with [insulated] [regular] rim, low flush flapper type flush valve, [Crane  Radcliffe 3-401, combination] [            ].

.2	Seat:  Solid plastic with closed front and cover, brass bolts, [Olsonite #30] [            ].

2.4	URINAL

.1	Urinal:  [Wall-hung, wash-out urinal with shields, integral trap] [Slope front stall urinal with] integral flush rim, removable SS strainer, 20 mm top spud, [Crane 7-72 Cromwell] [Crane 7-32 Sanitor] [            ].

.2	Flush Valve:  Chrome plated, diaphragm type with [oscillating handle], [push plate] escutcheon, integral screwdriver stop, [vacuum breaker], [Presto 451 VB] [            ].

.3	Metering Valve:  Chrome plated, with [oscillating handle] [push button] screwdriver stop, [vacuum breaker] [Waltec 86T Tempus] [            ].

.4	Tank:  Insulated with bottom supply and siphon valve, [Crane Belmont 7 - 170 1/2] [            ].

2.5	URINAL - WATER EFFICIENT

.1	Urinal:  Wall-hung, wash-out type for low flush water volume, removable SS strainer, [Crane 7-133 Ambassador] [            ].

.2	Flush Valve:  Chrome plated, diaphragm type, escutcheon integral screwdriver stop and 6 litre flush volume [Torpedo 4045 ultra low flush] [            ].

2.6	LAVATORIES

.1	Lavatory:  Wall-hung 500 x 450 mm minimum, with minimum 100 mm high back, drillings on 100 mm centres, rectangular basin with splash lip and overflow, [Crane Norwich 1-208] [            ].

.2	Lavatory:  Wall-hung 480 x 450 mm minimum, with shelf back, drillings on 100 mm centres, rectangular basin with splash lip and overflow, [Crane Closin 1-700] [            ].

.3	Lavatory:  Self-rimming countertop 480 x 400 mm minimum with drillings on 100 mm centres, overflow, [Crane Marquis 1-346] [      ].

.4	Trim:  Chrome plated supply fitting with Chain and plug, aerator, indexed blade handles [Delta Delex 2500] [            ].

2.7	BARRIER-FREE LAVATORIES

.1	Lavatory:  Wall-hung 508 x 584 mm minimum, with low shelf back, drillings on 100 mm centres, rectangular basin with splash lip and front overflow [Crane Ch-8051] [            ].

.2	Trim:  Chrome plated concealed supply fitting with gooseneck spout, [Chain and plug] [grid strainer], aerator, indexed 70 mm lever handles, insulated bent tailpiece, offset waste and trap [Crane Ch-8051] [            ].

.3	Lavatory:  Self-rimming countertop 480 x 400 mm minimum with drilling on 100 mm centers, overflow, [Crane Marquis 1-346] [            ].

2.8	SHAMPOO SINK

.1	Countertop:  Built-in white [      ] bowl, front scooped rim, rolled neck rest, raised back ledge, with 90 mm crumb cup strainer.  Bowl size 500 x 535 x 250 m [Belvedere 3800] [            ].

.2	Trim:  Separate shampoo spray nozzle and disappearing hose [Belvedere, Dialect Flo-Temp #622] [            ].

.3	Trap:  Chrome plated bronze hair and sediment interceptor, removable chrome plated bronze cleanout cover.

2.9	STAINLESS STEEL SINKS

.1	Bowl:  520 x 510 x 180 mm O.D., Type 302SS, self-rimming, single compartment with undercoating, 90 mm crumb cups, [2] [3] [4] hole drilling in ledgeback, [Kil Steel Queen QL2] [            ].

.2	Bowl:  790 x 510 x 180 mm O.D., Type 302SS, self-rimming, double compartment with undercoating, 90 mm crumb cups, [2] [3] [4] hole drilling in ledgeback, [Kil Steel Queen QDL2]  [            ].

.3	Trim:  Chrome plated supply with swing spout, aerator, indexed lever handles [and retractable spray], [Crane Citadel, [C-5061-L] [C-5073-L]] [            ].

2.10	BATHTUB [AND SHOWER]

.1	Bathtub:  1530 mm nominal size, actual size 1524 mm, stain resisting, porcelain finish steel bathtub with slip resistant surface, [Crane 2-142 Chateau] [            ].

.2	Bathtub Trim:

.1	Concealed shower and overrim supply.

.2	Pressure balancing mixing valve with maximum temperature limit, integral stops and lever handle.

.3	Diverter spout with side outlet for handheld shower.

.4	Wall/hand shower head with on-off control, vacuum breaker, chrome swivel elbow, 1500 mm flexible metal hose and [Two wall hooks. Symmons Model S-96-400 - 1071-XL] [760 mm slide bar. Symmons 96-400-1071-XL- B30].

SPEC NOTE:  Specify slide bar for Barrier-free trim.

2.11	SHOWER CABINET

.1	Cabinet:  840 x 810 x 2060 mm high fibreglass cabinet with 'Gelcoat surface' integral soap dish, and safety glass door with stainless steel piano hinge [Cabinet - Valley Fibrebath SS32] [            ].

.2	Trim:  Concealed shower supply with pressure balancing mixing valve and maximum temperature limits with integral stops and integral volume control, bent shower arm with adjustable spray ball joint shower head and escutcheon, wall mounting flange for fibreglass stall [Symmons S-96-1XFG] [            ].

2.12	SERVICE OR MOP SINKS

.1	Bowl:  600 x 600 x 250 mm deep white moulded stone, floor mounted sink with 25 mm wide shoulders, SS strainer, [Fiat MSB-2424] [            ].

.2	Trim:  Exposed wall type supply with cross handles, spout wall brace, vacuum breaker, hose and spout, strainers, eccentric adjustable inlets, integral screwdriver stops with covering caps and adjustable threaded wall flanges, [Crane CH-8560]  [            ].

.3	Provide 1.5 m of 15 mm plain end reinforced rubber hose, hose clamp, mop hanger.

3.	Execution

3.1	INSTALLATION

.1	Install each fixture with its own trap, removable for servicing and cleaning.  At completion thoroughly clean plumbing fixtures and equipment.

.2	Provide chrome plated rigid or flexible supplies to fixtures with screwdriver stops, reducers and escutcheons.

.3	Install wall mounted fixtures with approved wall carriers to suit installation.

.4	Mount wall-hung fixtures the following heights above finished floor:

Urinal:	Standard	550 mm to top of bowl rim.

Handicapped	480 mm to top of bowl rim.

Lavatory:	Standard	780 mm to top of basin rim.

Handicapped	800 mm to top of basin rim.

.5	Solidly attach floor-mounted water closets to floor with lag screws through mounting plate.  Do not use lead flashing, wax seal only.

.6	Install hose and faucets and hose connections with vacuum breakers.

.7	Provide wheelhandle isolation valves to all fixtures.

.8	Protect fixtures against use and damage during construction.

3.2	FIXTURES ROUGH-IN SCHEDULE

.1	Rough-in fixture piping connections in accordance with following table of minimum sizes or as required for particular fixtures.

| Description | Hot Water | Cold Water | Waste | Vent |
| --- | --- | --- | --- | --- |
| Lavatories | 13 mm | 13 mm | 40 mm | 30 mm |
| Service Sink | 13 mm | 13 mm | 50 mm | 40 mm |
| Kitchen Sink | 13 mm | 13 mm | 40 mm | 30 mm |
| Water Closet (Tank Type) | - | 13 mm | 100 mm | 50 mm |
| Urinals (Flush Valve) | - | 20 mm | 50 mm | 40 mm |
| Urinal (Tank Type) | - | 13 mm | 50 mm | 40 mm |
| Floor Drains | - | - | 100 mm | 40 mm |
| Hose Bibbs | 20 mm | 20 mm |  |  |

END OF SECTION