Section Cover Page

Section 32 17 23 2018-03-15 Pavement Markings

Use this Section to specify traffic paint lines on pavement.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

  - Related Requirements

1.2 	Reference Documents

1.3 	Submittals

1.4	Quality Assurance

1.5	Delivery, Storage and Handling

1.6	Sequencing and Scheduling

2.	Products

2.1	Materials

2.2	Traffic Marking Paint Systems

3.	Execution

  - Protection of Existing Work

  - Preparation of Substrate

3.3	Application of Pavement Line Markings

3.4	Clean-up

3.5	Protection of Completed Work

1.	General

1.1	RELATED Requirements

.1	Asphalt Concrete Pavement:	Section 32 12 16.

  - REFERENCE DOCUMENTs

SPEC NOTE:  Specify paragraph 1.3.1.1  for new work or paragraph 1.3.1.2  for maintenance work or both as required to suit project. Always include paragraph 1.3.1.3.

.1	The following documents, referenced in this Section, are published by the Master Painters Institute (MPI)

| .1 | Architectural Specification Manual |
| --- | --- |
| .2 | Maintenance Repainting Manual |
| .3 | Approved Product List |

1.3	SUBMITTALS

.1	Comply with requirements of [Section 01 33 00 – Submittal Procedures] [Division 01].

.2	Submit product data for traffic marking paint, including MPI product number.

1.4	Quality Assurance

SPEC NOTE:  Specify paragraph 1.5.1  for new work or paragraph 1.5.2  for maintenance work or both as required to suit project.

.1	Materials and workmanship for new work shall meet or exceed requirements of the APS Manual.

.2	Materials and workmanship for maintenance work shall meet or exceed requirements of the MR Manual.

1.5	DELIVERY, STORAGE, AND HANDLING

.1	Deliver materials in sealed original labeled containers bearing manufacturer's name, type of material, brand name, colour designation.

1.6	SEQUENCING AND SCHEDULING

SPEC NOTE:  Include this article when work of this Section may interfere with access to and use of buildings.

.1	Sequence and schedule work so as to provide access to building[s] at all times.  Arrange work so as not to interfere with normal use of premises.

- Products

  - materials

.1	Materials are specified by the designated MPI systems, with colours specified herein.

.2	Only products listed in the MPI “Approved Product List” are acceptable for use.

2.2	TRAFFIC MARKING PAINT system

.1	System for New Work:  [EXT 2.1A, Latex] [EXT 2.1B, Alkyd], [yellow] [white] [   ] colour.

.2	System for Maintenance Work: [REX 2.1A, Latex] [REX 2.1B, Alkyd], [yellow] [white] [   ] colour.

3.	Execution

3.1	PROTECTION OF EXISTING WORK

.1	Protect structures, buildings, sidewalks, landscaping and other surface features against spillage and over-spray during painting operation.

  - Preparation of substrate

SPEC NOTE:  Specify paragraph 3.2.1  for new work or paragraph 3.2.2  for maintenance work or both as required to suit project.

.1	Prepare new pavement in accordance with manufacturer’s instructions and in accordance with "Architectural Painting Specification Manual", Chapter 2,  Section 3.

.2	Prepare for maintenance repainting for the existing degree of surface deterioration (DSD) in accordance with "Maintenance Repainting  Manual", Chapter 2,  Section 3.

3.3	APPLICATION OF PAVEMENT LINE MARKINGS

.1	Clean pavement surface as recommended by paint manufacturer.

.2	Paint lines straight and in uniform width, at locations indicated on drawings.

.3	Apply paint using marking machine or line stencil, and as recommended by manufacturer, to minimum 0.18 mm dry film thickness.

.4	Line Width:

.1	Roadways and Parking Areas:  [100][150] mm, except where otherwise indicated.

.2	Athletic Courts:  [   ] mm.

3.4	CLEAN-UP

.1	Remove spillage and over-spray of paint from pavement, sidewalks, building and other site features.  Use methods and materials without damaging and leaving visible residue on substrates.

3.5	PROTECTION OF COMPLETED WORK

.1	Keep traffic off pavement markings for a time as recommended by paint manufacturer.

END OF SECTION