Section Cover Page

Section 32 93 00 2012-06-15 Landscape Planting

Refer to “LEED Notes and Credits” page for additional guidance for LEED projects. Delete LEED items if project: .1 is excluded by the Department’s policy on LEED, or .2 the Department has determined that the work of this Contract is not to attain a LEED rating.

This Master Specification Section contains:

.1	This Cover Page

.2	Specification Section Text:

1.	General

1.1	Related Requirements

1.2	Reference Documents

1.3	Submittals

1.4	Measurement and Payment

1.5	Quality Assurance

1.6	Examination

1.7	Permits, Codes and Regulations

1.8	Delivery, Storage and Handling

1.9	Soil Analysis

1.10	Maintenance Period

1.11	Warranty

2.	Products

2.1	Plant Materials

2.2	Soil

2.3	Water

2.4	Planting Media

2.5	Planting Accessories

3.	Execution

3.1	Site Preparation

3.2	Preparation of Plant Beds and Tree Pits

3.3	Planting

3.4	Supporting Trees

3.5	Pruning

3.6	Protection

3.7	Maintenance And Plant Establishment

3.8	Maintenance Log Requirements

3.9	Final Acceptance And Termination Of Maintenance

3.10	Clean-Up

1.	General

1.1	RELATED Requirements

.1	Topsoil Placement and Grading:	Section 32 91 19.

.2	Seeding:	Section 32 92 19.

.3	Sodding:	Section 32 92 23.

.4	Exterior Landscape Maintenance:	Section 32 99 00.

1.2	REFERENCE Documents

| .1 | Nomenclature: to "International Code of Nomenclature for Cultivated Plants". |
| --- | --- |
| .2 | Canadian Standards For Nursery Stock: latest edition by Canadian Nursery Landscape Association (CNLA). |
| .3 | Clean Plants Standard (latest version): program administered by the Canadian Nursery Certification Institute with approval and support of the Canadian Food Inspection Agency. |
| .4 | Alberta Yards & Gardens, What to Grow: published by Alberta Agriculture and Rural Development, Agdex 200/32-1. |
| .5 | Canadian System of Soil Classification: latest edition by Agriculture and Agri-Food Canada. |
| .6 | ANSI A300: pruning standards and practices of the International Society of Arboriculture. |

1.3	SUBMITTALS

SPEC NOTE:  Edit item to suit project requirements.

.1	[Conform to requirements of Section 01 33 00 – Submittal Procedures].  Submit the following, for Minister’s review and approval as applicable:

.1	Copies of all permits and licenses required by regulatory authorities prior to commencement of work.

.2	Samples of all topsoil, soil mix, mulch, and other organic materials intended for use.  Samples to weigh between 500 g and 1 kg and be packaged in clean containers with label indicating source of material, date of sampling and project name.  Samples to be typical of the lot of material to be supplied and provide an accurate indication of colour, texture and organic content.

.3	Submit list of all plant nursery sources.  Where applicable, provide “Clean Plants Certification Number” of each Clean Plants certified nursery for approval.  Submit information minimum two weeks prior to commencement of work.

.4	Samples of planting accessories and materials including source of supply as specified or as directed by Minister.

.5	Site supervisor’s credentials prior to commencement of work.

.6	Work schedule showing approximate dates for commencement and completion of each item of work.  Submit prior to commencement of work.

.7	Submit all other required information and documents as requested or specified.

1.4	MEASUREMENT AND PAYMENT

SPEC NOTE: Edit specification item to suit contract and payment / measurement conditions.

.1	Unit Price Contracts:

.1	Each item of work in the unit price schedule will be paid at contract unit bid price.  Unit bid price shall include full compensation for all materials, equipment, labour and incidentals necessary to complete each unit item of work.

.2	Monthly progress payments made for unit price bid and measured quantities of work will be subject to Minister’s review and acceptance of Contractor’s workmanship and performance.  Contractor shall ensure all work has been completed in accordance with contract specifications.

.2	Stipulated Price (Lump Sum) Contracts:

.1	For payment purposes, all landscape work in contract will be paid in accordance with the following guidelines:

.1	[Seventy-five (75%)] [Eighty (80%)] [Eighty-five (85%)] [           ], of the landscape contract value will be deemed to be allocated for supply and placement of landscape materials and related work specified in contract documents.

.2	Remaining [twenty-five (25%)] [twenty percent (20%)] [fifteen percent (15%)] [           ], of the landscape contract value will be deemed to be allocated for landscape maintenance and warranty services specified in contract documents.

.3	Monthly progress payments will be made for work satisfactorily completed in accordance with contract specifications.  Payment will be subject to Minister’s review and acceptance of Contractor’s workmanship and performance.

.4	Work that the Minister determines to be improper, inadequate, incomplete and not in accordance with contract specifications will not be accepted.

# 1.5	quality assurance

.1	Contractor:   experienced and knowledgeable in landscape work of contract.

.2	Site Supervisor:  competent, experienced and knowledgeable to direct and supervise all staff and work of contract.  Supervisor shall possess a Landscape Journeyman Gardner certification or other similar qualification acceptable to Minister.  Submit supervisor’s credentials for Minister’s approval prior to commencement of work.

.3	Staffing:   experienced, competent and trained landscape personnel who will perform all tasks and services in a knowledgeable and professional manner.  Workers shall act safely and professionally at all times while working on site.  Contractor shall not assign any worker that the Minister deems incompetent, careless, insubordinate, or otherwise objectionable to work on site.

.4	Contractor shall be responsible for ensuring that contract specifications are being adhered to.  Failure of the Minister to immediately reject unsatisfactory workmanship or to notify the Contractor of their deviation from the specification shall not relieve the Contractor of their responsibility to repair and/or replace unsatisfactory work.

.5	Contractor shall obtain approvals as required by contract for suppliers, sub-contractors, and all materials.

.6	Pre-Construction Conference:  prior to commencement of work, Contractor shall meet with Minister to review overall work of contract and this section.

1.6	examination

.1	Contractor shall advise Minister, in writing, of any conditions or defects encountered on site before or during construction upon which the work of this section depends and which may adversely affect its performance.

.2	Do not commence work until adverse conditions or defects have been evaluated by the Minister and corrective measures taken.

.3	Commencement of work shall imply acceptance of existing surfaces and conditions and no claims for damages or extras resulting from such conditions or defects will be accepted later, except where such conditions could not have been known prior to commencing work.

1.7	permits, codes and regulations

.1	Contractor shall obtain and pay for all permits and fees as required by Local Authority and prevailing ordinances and/or codes to fully complete the Work.

.2	Contractor shall comply with all existing laws, codes, ordinances and regulations which in any way affect the conduct of the work.

1.8	DELIVERY, STORAGE AND HANDLING

.1	Handle plants with care and skill to prevent injuries to trunk, branches, roots, rootballs and containers.  Trees with damaged, broken or abraded trunks or branches may be rejected.

.2	Protect plants during shipment with windscreen or other suitable covering.  Carefully tie in all branches before transporting.  Take all precautions to prevent excessive drying from sun and wind and breakage from wind and equipment during transport.  All points of contact between plant and equipment shall be protected with pads.

.3	Adequately protect plants in storage from drying out, frost damage, exposure of roots to sun, injury and breakage resulting from equipment and severe winds, site vandalism and other damages.

.4	Install plants within 24 hours of delivery to site.  Store and heel plants in with topsoil or mulch in suitable location when planting cannot be completed on time.  Keep all plants moist until planted.  Plants not planted within required timeframe, weather permitting, may be deemed unacceptable by Minister.

.5	Do not install plants whose soil balls have been cracked or broken or when burlap ropes used in connection with transplanting have been removed.  Do not use plants damaged during contact with equipment, or plants that are wilted, windburned or stressed.

.6	Replace damaged or rejected plants at no cost to Minister.

.7	Do not transport trees in open trucks when the temperature is in excess of 25oC, or at speeds in excess of 60 km/h.

1.9	SOIL ANALYSIS

SPEC NOTE:  Select whether Minister or Contractor will be responsible for testing of imported topsoil and soil mix including testing of native stockpiled topsoil.  Edit item as necessary.

.1	Imported Soil:  [Minister] [Contractor] will arrange and pay for services of accredited testing laboratory to perform horticultural soil analysis on each source of soil mix and topsoil supplied by Contractor.

.2	Contractor shall be responsible for ensuring all samples of imported soil are submitted for testing well in advance of commencement of work.  Imported topsoil and/or soil mix shall not be placed on site until approved by Minister.

.3	Native Stockpiled Topsoil:  [Minister] [Contractor] will arrange and pay for services of accredited testing laboratory to perform horticultural soil analysis on stockpiled native topsoil, where applicable.

.4	Soil analysis for horticultural use shall include results for: existing major soil nutrients;  soil pH value; total soluble salts (electrical conductivity); percentage of organic matter;  soil texture and percentage of sand, silt and clay;  nutrient recommendations; and recommendations for soil amendments.

.5	Minister reserves the right to inspect and evaluate all sources of imported soil selected by Contractor.

.6	Contractor to submit original copies of soil analysis reports to Minister as required.

1.10	MAINTENANCE PERIOD

SPEC NOTE: Edit as necessary to suit contract.  Generally, when maintenance requirements are for more than eight weeks, use of Section 32 99 00 - Exterior Landscape Maintenance is recommended in tender documents except for smaller landscape projects.  Edit item accordingly, indicating length of maintenance period in contract and specify all other conditions pertaining to the maintenance period.

.1	[Maintain plant material from time of planting until minimum eight [       ] weeks, three [       ] months, one year after Date of Interim Acceptance of the landscape portion of Work in Contract].

[OR]

.1	[Maintain exterior landscape work for a minimum of two years, inclusive of two full and complete growing seasons (May 1st to October 31st ) commencing from Date of Interim Acceptance of the landscape portion of Work in Contract.  See Section 32 99 00 – Exterior Landscape Maintenance for all maintenance requirements and details].

.2	Maintenance services shall be performed during the landscape growing season (May 1st to October 31st).  Minister, however, reserves the right to determine actual date of commencement and termination of maintenance based on existing climatic conditions, soil moisture and plant health.

.3	Any additional maintenance beyond the specified maintenance and warranty period required for Contractor to achieve final acceptance shall be provided at Contractor’s own expense.

.4	Any incomplete weeks or months of maintenance shall be carried over to the following landscape growing season.

.5	Minister reserves the right to extend maintenance period and/or reduce monthly progress payments for maintenance services any time Contractor fails or neglects to provide proper and adequate maintenance services in accordance with contract specifications as determined by Minister.

1.11	WARRANTY

SPEC NOTE: Edit to indicate length of warranty period in contract.  Landscape warranty in contracts having an extended maintenance period over one year in length shall generally match the length of maintenance period in contract.  Determine and edit if additional warranty is required for all replacement plants.

.1	[Contractor shall provide warranty for all plant materials, related works and other materials for a minimum period of one year.  Warranty period shall commence from date of Interim Acceptance of the landscape portion of Work in Contract].

[OR]

.1	[Contractor shall provide warranty for all plant materials, related works and materials for a minimum period of two years, inclusive of  two full and complete growing seasons (May 1st to October 31st) commencing from the Date of Interim Acceptance of the Work].

.2	Minister reserves the right to extend Contractor’s warranty responsibilities for an additional one year on all replacement plants and for all original plants where leaf development, colour and growth are not sufficient to ensure future survival.

.3	During warranty period, Contractor shall remove and replace all plants which are dead, unhealthy, unappealing, weak, or in unsatisfactory growing condition or in any other way that do not meet the requirements of the specifications or that show more than 25% dead or unhealthy growth.

.4	Supply and installation of warranty replacement plants shall be performed by Contractor in accordance with contract specifications.  All plants not found in a healthy thriving condition must be immediately removed from site and replaced during the warranty period.  When directed by Minister, plant replacements shall be completed within seven (7) days of notification.

.5	Minister shall be sole judge as to condition of plant material regarding warranty replacements.

- Products

2.1	PLANT materials

SPEC NOTE: Edit to suit project.  Smaller landscape projects may not necessarily require plant material from a “Clean Plants Certified Nursery”.

.1	Source Quality Control:

.1	All plants to be true to genus, species and cultivar specified and grown in a recognized nursery in accordance with good horticultural practices as advocated by the Canadian Nursery Landscape Association.  [Each plant nursery shall be a “Clean Plants Certified Nursery” approved by the Canadian Nursery Certification Institute].

.2	[Plants grown in a “Clean Plants Certified Nursery” to have been grown and handled in accordance with the Clean Plants Standard developed by the Canadian Nursery Certification Institute and the Canadian Food Inspection Agency.  Submit “Clean Plants Certification Number” of each certified nursery for verification].

.3	Supply ball and burlapped trees that have been nursery grown in Alberta for a minimum of five years to ensure hardiness.

.4	Supply container grown shrubs, herbaceous perennials, ground covers and other plants that have been nursery grown under a similar climatic zone to those in locality of project.

.5	Plant supply to conform to federal and provincial regulations.

.6	Trees and other plants will be inspected and selected by Minister from local nursery source of supply or place of growth prior to digging and delivery to site.  Contractor’s representative shall be present during inspection.  Minister will tag acceptable plants with cargo seal tags or other suitable tagging material.

.7	Where formal arrangements or consecutive order of trees or other plants are required in plan, all required plant material shall be selected for a uniform height and spread.  Minister reserves the right to reject all plants at source if available plant quantity is inadequate.

.8	Minister reserves the right to reject any plant where tags have been removed before plants have been planted on site and approved by Minister.

.9	Approval of plants at source does not impair the right of Minister to inspect plants on site during progress of work.  Any plant which has been damaged by pests or mechanical equipment; substituted without authorization; injured by any means or cause; or does not conform to specifications must be removed from site whether in place or not and replaced with acceptable plant material as directed by Minister.

.10	Plant substitutions are not permitted unless approved by Minister.  Contractor shall submit verifiable and adequate proof that specified plants are not available or of unacceptable quality before requesting plant substitutions.

.2	Condition and Quality:

.1	Plants shall be of specimen No. 1 grade and quality, exceptionally heavy, and so trained or favoured in development and appearance as to be unquestionably and outstandingly superior in form, compactness, branching and symmetry.  Plants shall exhibit vigorous growth, be well branched and densely foliated when in leaf; free of disease, insects, eggs, or larvae; free of dead branches and dead branch tips; and have healthy, well developed root systems.

.2	Trees with multiple leaders;,with damaged, broken or crooked leader, weak “Y” crotches, bark abrasions or scars, sun-scald, frost cracks, disfiguring knots, insect damage or infestations are not acceptable.

.3	Tree trunks shall be clean and free of stubs, decay, splits or other damage.  Root collar shall be free of defects, including circling, kinked and stem girdling roots.

.4	Specific tree requirements include:

.1	Deciduous Trees:  straight bodied trees according to their natural habit of growth; having a balanced and well branched head; and with leaders intact, undamaged and uncut.  Height of branching shall be consistent.

.2	Coniferous Trees:  straight central leaders with a dense, heavy and uniform crown; well branched to ground level; and having outstanding natural colour.  Trees with a sparse or thinly layered branched structure or with a unnaturally sheared appearance are not acceptable.

.3	Clump Form Trees:  three or more trees planted as a group that have grown together to form a single tree having three or more main stems or trunks.  Clump trees shall be low-branched; have a unified and well established root system; and have well developed crowns.

.4	Multi-Stem Trees:  with three or more main stems originating from a single root crown or from a point just above the root crown.  Trees shall be low-branched; have a unified and well established root system; and have well developed crowns.

.5	Shrubs:  natural form, typical of genus, species and variety; minimum of four canes or primary stems that start from the ground.

.6	Herbaceous Perennials:  healthy and vigorous crowns, well rooted and established, not less than two years old and twice transplanted.

.7	Vines:  healthy, vigorous and well rooted in container, not less than 3 runners at 50 cm length or more.

.8	Ground Covers:  healthy, vigorous, well rooted and established in container.  Size proportionate to root development.

.9	Heeled-in plants or plants from cold storage are not acceptable.  Plants that have been top worked, unnaturally sheared or colour treated are not acceptable.

.10	Collected Plants:  native plants indigeneous to area.  Plants designated as collected plants on plan shall be dug with root balls minimum 20% larger than for nursery grown stock.  Well developed crowns and branching.

.3	Plants – Container Grown Nursery Plants:

.1	Container grown plants shall conform to measurements and container size specified.  Measure height and spread, in centimetres, with branches in their normal positions in accordance with Canadian Standards For Nursery Stock. Plants shall possess normal balance between height and spread.

.2	Plants shall be grown in sufficiently sized containers for minimum of three months in accordance with Canadian Standards For Nursery Stock.

.3	Container grown stock shall be healthy, vigorous, well rooted and established in container.  Container grown plants shall have a well established root system reaching sides of container to maintain a firm ball when container is removed but shall not have excessive root growth encircling the inside of container.  Over established and root bound plants in containers are not acceptable.

.4	Plants shall have nursery labels containing the correct botanical name.

4		Plants - Balled and Burlapped:

.1	Supply balled and burlap trees in wire baskets that conform to plant measurements specified on plan.  Measure height and spread, in centimetres, with branches in their normal positions in accordance with Canadian Standards For Nursery Stock.

.2	Caliper Size:  caliper measurements, in millimetres, shall be the determining measurement.  Measure deciduous tree caliper 15 cm above ground on trees up to 100 mm caliper size.  Larger sized trees, 100 mm caliper and over, shall be measured 30 cm above ground.

.3	Clump Form / Multi-Stem Tree Measurement:  caliper measurements shall be in accordance with Canadian Standards For Nursery Stock.

.4	Coniferous Height:  height measurement shall be taken at midpoint between the uppermost whorl and the tip of the leader.

.5	Trees shall be properly machine dug with firm and natural root balls at minimum size and shape as specified in Canadian Standards For Nursery Stock.  Root balls shall be placed, firmly wrapped and secured, in burlap lined wire baskets with rope or rottable twine.  Root collar shall be apparent at surface of root ball.  Plant trunks shall be in centre of root ball.

.6	Root ball size shall be sufficiently large to contain at least 75% of fibrous root system with a ball depth not less than 50% of ball diameter.

.7	Undersized, broken, loose, manufactured or other defective root balls will be rejected.  Root balls shall be free from pernicious perennial weeds and grass and their roots.

.8	Adjust root ball size according to growing habits of plants.  Clump form and  multi-stem trees and coniferous pine trees shall be machine dug with root balls minimum two sizes larger than standard trees in accordance with Canadian Standards For Nursery Stock.

.9	Trees 150 mm caliper and over shall be root pruned during previous two successive growing seasons prior to delivery.

2.2	WATER

.1	Water:  clean, fresh, and free of substances or matter that would inhibit vigorous and healthy plant growth.

.2	Contractor shall supply clean water, equipment, methods of transportation, water tanker, hoses, attachments, and other accessories as necessary to adequately apply water to all plant material and for other work in contract.

.3	All costs for supply of water incurred during the contract period shall be borne by Contractor.

.4	[Minister will make available a limited supply of water from building source at no cost to Contractor.]

2.3	SOIL

.1	Topsoil:  fertile natural loam, capable of sustaining healthy growth.  Topsoil to be loose and friable, free of subsoil, clay lumps, stones, live plants, roots or any other deleterious material greater than 20 mm diameter, free of litter, foreign matter and toxic materials harmful to plant growth.  Topsoil containing construction debris, sod clumps, quackgrass or other noxious weeds is not acceptable.  Topsoil to meet the following requirements:

.1	Minimum 6% organic matter.

.2	Acidity/alkalinity shall range from 5.9 pH to 7.0 pH.

.3	Electrical Conductivity (E.C.) - level of soluble salts shall not exceed 1.5 dS/m.

.4	Texture:  “Loam” topsoil in accordance with Canadian System of Soil Classification.  Topsoil to fall within an allowance of (2% of the values stated in the table below:

| Soil | Sand (%) | Silt (%) | Clay (%) | Class |
| --- | --- | --- | --- | --- |
| Topsoil | 35 | 35 | 30 | Loam |

SPEC NOTE:  Delete Item 2.3.2 if no suitable native stockpiled topsoil exists on site.

.2	[Native Stockpiled Topsoil:  native topsoil stockpiled on site is available for use in this contract.    Prior to use, Contractor shall eliminate all existing weed and foreign grass growth and screen the soil using approved screener.  Amend native stockpiled topsoil to comply with soil specifications required in contract.]

.3	Peat Moss:  decomposed plants, fairly elastic and homogeneous, free of decomposed colloidal residue, wood, sulphur and iron.  Minimum of 80% organic matter by mass, pH value between 4.5 and 6.0.  Furnished in an air-dry state, packed in standard bags or bales showing name of manufacturer.

.4	Sand:  washed course sand, medium to course textured, free of impurities, chemical or organic matter.

.5	Bonemeal:  finely ground commercial bonemeal with minimum analysis of 4% nitrogen and 20% phosphoric acid.

2.4	PLANTING MEDIA

.1	Soil Mix:  3 parts fertile topsoil; 1 part horticultural peat moss; 1 part sharp sand;

bonemeal – apply at 0.6 kg/m3 soil mix or 50g/m2 soil mix and thoroughly mix into soil.

.2	Fertile Topsoil:  fertile natural loam, capable of sustaining healthy growth.  Supply topsoil as specified.  Mix bonemeal fertilizer into topsoil at 0.6 kg/m3 of soil.

2.5	PLANTing ACCESSORIES

SPEC NOTE: Edit planting accessories item and specify only those accessories that are actually required in contract.  Ensure type of shredded bark mulch is indicated.

.1	Support posts:  T-rail studded 40 mm x 40 mm metal stakes, minimum 2.1 m long.  Stakes shall be scaled, primed and painted [as directed by Minister].

.2	Guy wire:  #12 or #14 pliable galvanized steel wire.

.3	Guy wire anchors:  T-rail metal stakes, minimum 700 mm long.  Paint minimum top 200 mm of stake with an orange fluorescent spray paint for visibility.

.4	Bark protector:  12 mm diameter new reinforced soft black rubber hose.  Hose shall be cut of adequate length to completely encircle tree trunk to ensure no wire contacts tree bark.  High grade flat grommeted fabric straps is acceptable in staking plants.  Hard plastic hose protectors are not acceptable.

.5	Flagging:  fluorescent orange flagging tape.

.6	Tree trunk guard:  flexible, expandable and self opening plastic spiral wrap manufactured for horticultural use.  Guard shall be of adequate length up to 60 cm high.

.7	Bark mulch:  premium shredded coniferous [pine] [fir] bark mulch.  Shredded bark mulch shall be approximately 50 mm or less in size.  Mulch shall be free of non-organic materials, wood preservatives, diseased wood, moulds, fungi and insect infestations.

.8	[PVC edging material:  heavy duty black polyethylene edger with heavy 25 mm top bead, bottom v-lip, 135 mm width, with anchor stakes, connectors and other installation accessories].

.9	Plant protection:  materials to protect plants from rodent, animal and sun damages.  Install galvanized wire mesh with fasteners; plastic perforated spiraled horticultural strips; burlap plant wrap with fasteners; or other approved materials in accordance with manufacturer’s instructions.

.10	[Gravel for planters:  20 mm washed crushed stone].

.11	[Geotextile fabric:  black heavy-duty woven polypropylene geotextile fabric complete with manufacturer’s installation accessories approved by Minister].

.12	[                      ]

3.	Execution

3.1	Site preparation

.1	Locate and stake locations of all subsurface utility lines and underground irrigation lines, where applicable.

.2	Protect bench marks and hubs which form part of legal site survey.

.3	Stake out locations of all trees and other major planting including outlines of plant beds with wood stakes or other acceptable material.

.4	Where conflict exists between underground services and proposed plantings, promptly notify Minister for instruction.  Adjustments to plant locations require Minister’s approval.

.5	Maintain offset distances when locating trees near underground services, adjacent to walkways, property lines, curbs, intersections, entrances, light standards, site signage and buildings or as directed by Minister.  Do not locate any tree within minimum 1.5 m of a ditch line.

.6	Obtain Minister’s approval of plant locations before installing any plant material.  Plants installed by Contractor without Minister’s approval of location shall be relocated at Contractor’s expense.

3.2	preparation of plant beds and tree pits

SPEC NOTE:  Edit as required for contract.

.1	Planting Beds:  excavate plant beds minimum of [450] [600] mm deep.

.2	Raised Planters:  excavate raised planters to [full depth of planter] [or] [minimum depth of [750] [600] mm.]

.3	Trees:  excavate tree planting pits minimum twice the diameter of the root ball and to full depth of rootball.  Excavation shall be large enough to provide placement of minimum 300 mm of fertile topsoil backfill around root ball.

.4	Obstructions:  notify Minister if underground construction debris, rock, hardpan soil stratum or other obstructions are encountered during plant pit excavations.

.5	Remove all excavated subsoil and foreign debris material from site.  Do not mix with planting soil or use as backfill.

.6	Do not excavate plant pits unless trees are scheduled for installation the same day.  Cover and/or clearly flag all excavated plant pits left unattended for any length of time that may present a hazard.

.7	Scarify:  scarify and roughen sub-grade soil within sides of excavated tree pit to minimum depth of 100 mm to eliminate smooth glazed walls.  In planting beds, scarify and loosen sub-grade soil within excavated plant bed to minimum depth of 150 mm.  Complete scarification of subsoil before placing any planting soil in tree pit or plant bed.

.8	Raised Planters:  place washed gravel over approved subgrade in raised planters to minimum compacted depth of 200 mm or as detailed on drawing.  Lay geotextile fabric over washed gravel before placing any soil mix.  Place soil mix in raised planters to a finish grade approximately 50 mm below top of planter wall after settlement.

.9	Soil Mix-Plant Beds:  place soil mix in planting beds to full depth of excavation and approximately 50 mm higher than adjacent finish grade.  Soil mix to be placed in appropriate layers and tamped to eliminate any settlement.  Slope grade away from building.

.10	Keep plant pit and plant bed excavations dry.  Remove excess water before planting.

.11	[Install PVC edging material in accordance with manufacturer’s instructions at edge of plant beds  and where indicated on drawing.]

.12	Obtain Minister’s approval for all excavation and soil placement requirements before proceeding with installation of plant material.

3.3	PLANTING

.1	During progress of work, Minister will review condition and quality of plants delivered to site and inspect Contractor’s workmanship and performance to ensure compliance with specifications.

.2	Set plants plumb in centre of pits and face for best appearance and relationship to adjacent structures.

.3	Container Grown Plants:  set plants in pit at same relation to grade as originally grown, after settlement has taken place.  Remove containers and gently separate or split roots before planting to ensure proper root development.  Plants installed below finish grade are not acceptable.  Thoroughly water plants after planting.

.4	Ball and Burlap Trees:  place plant straight in pit on undisturbed soil  Root ball shall be placed so that top of root flare is slightly above finish grade after settlement has occured.  Trees planted too deep with root flare below grade will be rejected by Minister.

.5	Backfill with fertile topsoil around rootball in layers of 150 mm and firmly tamp to eliminate voids and air pockets.  Ensure all trees have minimum 300 mm of topsoil surrounding the sides of the root ball.

.6	When tree pit is approximately 1/2 full of topsoil, thoroughly water planting hole allowing water to completely penetrate planting soil.

.7	Wire Basket:  cut and remove all wire, burlap, rope or twine from minimum upper top one-half (1/2) of root balls.  Remove all wire basket debris from site; do not bury in tree pit.  Trees planted without removal of wire basket will not be accepted by Minister.

.8	Complete backfilling around root ball to final grade in layers only after wire basket and other materials have been removed.  Firmly tamp topsoil in place.

.9	Construct a neat circular water retention saucer surrounded by a soil embankment at outside edge of root ball or as directed by Minister.  In boulevards, parking islands and other confined locations adjust size of saucer to suit location and maintenance issues.  Fill saucer with water and allow it to be completely absorbed.  Place additional planting soil as necessary where settlement occurs.  Thoroughly deep root water all plants.

.10	Slope Planting:  place top of root crown at or slightly above finish grade at centre of plant pit.  Form a saucer on downhill side to catch and retain water and to control erosion.

.11	After water has been completely absorbed, cover tree watering saucer with 100 mm of shredded bark mulch.  Taper mulch to ground level at trunk.

.12	Place bark mulch to 100 mm depth over planting beds.  Keep mulch material away from trunks and stems of plants.

.13	Install tree trunk guard around base of deciduous tree trunks that are planted in turf areas to protect from mechanical damage.

3.4	SUPPORTING TREES

.1	Support trees immediately after installation.  Install minimum two support posts on deciduous trees 80 mm in caliper and under and on coniferous trees 3.0 m in height and under.  Place support posts on prevailing wind side of tree and directly opposite.  Larger trees shall require additional support posts spaced equally around tree as necessary.

.2	Anchor support post minimum 450 mm into undisturbed ground.  Ensure support posts are secure and vertical.  Replace all damaged support posts.

.3	Locate support posts away from trunk and branches.  Height of support shall correspond with tree height.  Support posts to be installed in a consistent direction.

.4	Provide each tree support with a bark protector and tie secured at approximately 60% of tree height.  Do not tie trees too tightly; allow tree to move in response to winds.  Keep plant plumb.

.5	Deciduous trees over 100 mm in caliper and coniferous trees over 3.5 m in height may require adequate staking using metal anchors and guy wires as directed by Minister:

.1	Guy with three double guys and anchors spaced equally around plant.

.2	Provide guy looped around plant trunk, encased in hose or rubber belting.

.3	Attach guys at 60% of plant height at angle of 45 degrees.

.4	Top of anchor to be flush with finished grade.

.5	Keep guys taut and plant plumb.

.6	Attach flagging tape to guys as safety precaution.

3.5	PRUNING

.1	Perform pruning in accordance with proper practices and standards (ANSI-A300) of the International Society of Arboriculture.  Pruning to be performed by a certified arborist unless approved otherwise by Minister.

.2	Prune to provide natural branching structure and to encourage healthy natural growth.  Do not prune terminal leader of plant or leave protruding stubs when pruning.

.3	Limit pruning to removal of dead or injured branches, stray branches, double leaders, water sprouts, suckers and to compensate for loss of roots as a result of transplanting.

.4	Do not strip lower branches, raise up crown of trees, top or shear any plant.

.5	Contractor shall remove improperly pruned plants and install acceptable replacement plants at Contractor’s expense if directed by Minister.

3.6	PRotection

.1	Take all necessary precautions to protect work in progress, all property, persons, hard surfaces, buildings and existing trees from any damage that might be incurred arising from this Contract.

.2	Protect all plant materials and other site work from all damage, disturbance, or other construction activity from date of commencement of work to final completion and acceptance of work.  Remove protection only after plants are properly established and accepted or as directed by Minister.

.3	Damaged or unhealthy plants and other work resulting from inadequate protection or watering shall be repaired or replaced as directed by Minister at Contractor’s expense.  All damages shall be corrected prior to final acceptance.

3.7	MAINTENANCE and plant establishment

SPEC NOTE: Edit specification to suit contract.  However, when maintenance requirements are for more than eight weeks, use of this specification item is not recommended except on smaller landscape projects.  On larger projects that require an extended maintenance period, use Section 32 99 00 - Exterior Landscape Maintenance in tender documents and edit this item to indicate that all maintenance / establishment requirements are included in Section 32 99 00 .

.1	Work of maintenance period shall be performed each week and as frequently during the week to enable the proper establishment of all new plants and other landscaping installed to ensure that required services and tasks are satisfactorily completed and sustainable.

.2	Watering:  apply adequate water to maintain healthy and vigorous growing conditions.  All plants shall be watered minimum twice per week depending on plant species, location, and weather conditions to maintain adequate soil moisture.  During hot dry weather, increase frequency of plant watering to maintain good plant health.  Apply water properly and sufficiently to root zone.

.3	Provide clean fresh water, water tanker, equipment, methods of transportation, hoses, sprinklers, and labour necessary to adequately and efficiently apply water to plants.  Record quantity of water supplied and applied to plants in maintenance log.

.4	Supply all necessary equipment, accessories and labour when using of building water sources.  Operate existing irrigation facilities, where applicable, to supplement other methods of watering plants.

.5	Deep root water all plants by October 15th for winter preparation.

.6	Cultivate non-mulched plant beds and tree pits in upper 40 mm of soil biweekly to maintain a loose friable soil.  Do not damage plants roots when cultivating.

.7	Remove and dispose of all debris, rubbish, and animal waste each week.  Eliminate perennial grass and weeds including their roots weekly.  Provide clean and well maintained appearances within all planting beds, tree wells and other planted locations.

.8	Edge plant beds evenly to depth of 100 mm monthly or as required to maintain original line and shape.  Replace or reinstall any damaged or loose edging material as necessary.

.9	Maintain plant accessories and soil saucers in proper condition.  Keep stakes and guy wires in proper repair and adjustment.  Maintain tree in an upright plumb condition.  Remove tree stakes after trees are self supporting.

.10	Repair disturbed mulch or replace to maintain original mulch depth and coverage.

.11	Install and maintain appropriate plant protection materials as necessary for protection of plant material.

.12	Straighten all plants that lean or sag.  Replant as directed by Minister.

.13	Control disease, insects and other pests using acceptable integrated pest management practices to reduce pesticide use.  However, when necessary apply chemical pesticides in accordance with manufacturer’s instructions and government regulations.

.14	Replacement Plants:  immediately remove all dead and unhealthy plants and install new healthy replacement plants during the maintenance and warranty period.  Do not allow dead and unhealthy plants to remain on site.  Place flagging tape on all replacement plants for identification.  Replacement plant material shall be properly established before achieving final acceptance.

.15	Maintenance Inspections:  during progress of the maintenance period, the Contractor and the Minister will conduct site inspections every 30 days or less to determine whether ongoing maintenance activities have been performed in accordance with specifications.  Any maintenance not performed by Contractor in a satisfactory manner shall be immediately completed to Minister’s satisfaction.

# 3.8	maintenance log requirements

SPEC NOTE: When Section 32 99 00 - Exterior Landscape Maintenance is used in tender documents, delete this entire item.

.1	Maintain and complete a maintenance log for each day of maintenance activity throughout maintenance period.

.2	Submit maintenance log data to Minister each week for verification and approval of services performed.  Contractor shall ensure maintenance log data is true and accurate.  Site supervisor must complete and sign maintenance log.

.3	Maintenance Invoices:  invoices submitted without verifiable maintenance log data to support invoice will not be accepted.  Minister will defer payment of Contractor’s invoice until maintenance services are deemed acceptable and in compliance with specifications as determined by Minister.

.4	Record all maintenance activities including date/time of activities, quantity of water supplied and applied on site, materials used and quantity in maintenance of plants, location where activities were carried out, number of employees and name of supervisor on site.

3.9	final ACCEPTANCE and termination of maintenance

.1	Minister may accept work at end of maintenance period provided:

.1	Plants meet requirements of the specifications.

.2	Plants are properly and adequately established.

.3	Plants are alive, healthy and free of all pest infestations.

.4	Plants are properly planted, staked and pruned.

.5	Plants are recently and thoroughly watered.

.6	Plant pits and beds are cultivated and free of weeds, grass and debris.

.7	Planting accessories are properly installed and in good condition.

.2	Contractor shall use specified materials to correct plant installations that do not comply with requirements for acceptance and continue with specified maintenance/establishment until deemed acceptable by Minister.

3.10	CLEAN-UP and repairs

.1	During work of contract, keep all hard surfaces clean and tidy.  Sweep and wash all walkways and other pavement surfaces to maintain clean appearances.  Clear soil and rubble from catch basins, manholes, valves and other hard surface features.

.2	Collect all litter and other debris from site as necessary during work of contract.

.3	Remove and dispose of excess soil and waste materials, including subsoil, foreign debris, pots, wire basket debris, plant wrapping debris, and unhealthy plant growth at approved disposal site.  Contractor shall be responsible for all disposal costs.

.4	Remove all plant nametags, plant labels, cargo seal tags and flagging tape prior to final inspection or as directed by Minister.

.5	Repair all damages resulting from Work of this Contract.

END OF SECTION