Use this Section to specify requirements for exterior landscape maintenance for Properties Division contracts.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Maintenance Scope of Work

1.2	Reference Documents

  - Hours of Work

  - Maintenance Log and Payments

  - Quality Assurance

  - Soil Analysis

1.7	Delivery, Storage and Handling

1.8	Examination of Site

1.9	Damage to Property

2.	Products

2.1	Fertilizer

2.2	Topsoil and Peatmoss

2.3	Water

2.4	Pest Control

2.5	Plant Protection Materials

2.6	Snow Fencing

2.7	Maintenance Schedule

2.8	Annual and Perennial Flowers

3.	Execution

3.1	General Workmanship

3.2	Spring Clean-up

3.3	Turf Maintenance

3.4	Tree and Shrub Maintenance

  - Annual and Perennial Flower Maintenance

  - Integrated Pest Management

3.7	Pests: Weed, Insect and Disease Control

3.8	Irrigation System Maintenance

3.9	Autumn Preparation

3.10	Cleanliness of Grounds

1.	General

1.1		MAINTENANCE SCOPE OF WORK

.1	Provide grounds maintenance services that result in aesthetically pleasing and desirable site appearances.  Maintenance services shall include all required tasks, equipment, labour, materials and incidentals necessary to satisfactorily complete the specified grounds maintenance services.  Work shall be performed to best horticultural and site cleanliness practices and standards acceptable to Minister.

1.2	REFERENCE Documents

| .1 | “Pruning in Alberta” published by Alberta Agriculture and Rural Development Agdex 270/24-1. |
| --- | --- |
| .2 | “Alberta Yards & Gardens, What to Grow” published by Alberta Agriculture and Rural Development, Agdex 200/32-1. |
| .3 | “Manual for Maintenance of Grounds” published by Alberta Infrastructure. |
| .4 | ANSI A300: pruning standards of the International Society of Arboriculture. |

1.3	HOURS OF WORK

.1	Perform maintenance work during regular working hours of 07:00 to 18:00, Monday to Friday unless directed otherwise by Minister.

.2	Obtain Minister's approval to perform maintenance outside of regular working hours.

1.4	Maintenance log and payments

.1	Complete maintenance log for each day of maintenance activity.

.2	keep daily maintenance log at Minister’s site office or as directed by Minister.  Site supervisor shall complete and sign maintenance log prior to leaving site and ensure data reflects day’s work record.  .

.3	Minister reserves the right to reduce monthly payments when:

.1	contractor submits false and inaccurate maintenance log data.

.2	unsatisfactory, inadequate or incomplete maintenance services are provided.

.3	inadequate or improper materials are supplied or used on site.

.4	contractor fails to perform required maintenance services to schedule.

.4	Record and update all maintenance activities including date/time of activities, materials and quantity used on site, location where activities were carried out, number of employees on site, name of supervisor and other relevant information.

.5	Contractor’s Invoice:  approval of invoice requires submittal of verifiable and accurate maintenance log data that supports maintenance services being invoiced.  All work and tasks being invoiced shall have been performed and completed in accordance with contract specifications to ensure payment.  Maintenance services and tasks being invoiced shall be subject to Minister’s review and approval.

# 1.5	quality assurance

.1	Regulatory Requirements:  perform work in accordance with all applicable laws, codes and regulations required by authorities having jurisdiction over such work and provide all permits required by local authorities.

.2	Site Supervisor:  shall be competent, experienced and knowledgeable to direct and supervise all staff and maintenance work of contract.  Supervisor shall possess a Landscape Journeyman Gardener certification or have other horticultural qualifications acceptable to Minister to work on contract.  Site supervisor shall be on site during work of contract.  If requested by Minister, submit supervisor’s credentials for approval prior to commencement of work.

.3	Weekly Site Visits:  provide adequate site visits each week with sufficient staff to ensure that all required maintenance services are performed and completed on schedule in accordance with specifications.

.4	Staffing:  provide experienced, competent, trained and adequate maintenance personnel to perform all tasks and services in a safe and professional manner.  Workers shall act appropriately and professionally at all times.  Contractor shall not assign any worker that the Minister deems incompetent, careless, insubordinate, or otherwise objectionable to work on site.

.5	Submittals:  submit all required and requested information and documents for Minister’s approval where applicable to work of contract.

.6	Equipment/Vehicles:  supply appropriate and well maintained equipment, tools and other accessories to efficiently and effectively perform and satisfactorily complete all required maintenance services.  Equipment shall have proper safety devices maintained at all times while in use.  If equipment is defective or unsafe and/or is being operated in an unsafe manner, the Minister shall direct the Contractor to remove such equipment and/or the operator from site.  Contractor’s vehicles shall be identifiable with company name and contact number.

.7	Site Security:  Contractor’s personnel shall carry personal identification at all times while on site.  Identification shall be presented when requested by Minister or other site security staff.  All employees must check in with Minister upon entering and leaving the premises where applicable.

.8	Employee Attire/Safety Vests:  all workers shall be properly and appropriately attired at all times.  Each employee working on site shall wear a reflective brightly coloured safety vest for safety and visibility.

.9	Safety Precautions:

.1	Contractor shall supply and ensure that all workers use appropriate personal protective equipment where there is a danger of injury and as required by Alberta’s Occupational Health and Safety Act, Regulations and Code.

.2	Contractor shall provide training and ensure all workers practice appropriate safety measures and safe use of tools and equipment in accordance with WHMIS (Workplace Hazardous Materials Information System).

.3	Minister reserves the right to have the Contractor remove any employee from site if not wearing personal protective equipment or if not practicing safe work procedures.

.10	Maintenance Inspections/Meetings:  Minister shall, at its discretion, conduct random site inspections throughout the maintenance period to evaluate work performed.  Site meetings shall be scheduled every month or less between the Minister and the Contractor to review and evaluate Contractor’s quality of work and performance.

1.6	soil analysis

SPEC NOTE: soil analysis requirements are considered extra work in contract if deemed necessary by Minister.  Contractor to submit a cost estimate to perform all soil tests requested by Minister.  Service shall only proceed if approved by Minister.  Minister reserves the right to obtain soil test services from others if necessary.

[.1	Perform horticultural soil tests at each turf and planting location selected by Minister.  Arrange and pay for services of an accredited testing laboratory approved by Minister.]

[.2	Submit copy of each soil test performed to Minister.  Review all results with Minister.]

[.3	Horticultural Soil Analysis:  shall include results for existing major soil nutrients; soil pH value; total soluble salts (electrical conductivity); percentage of organic matter; soil texture and percentage of sand, silt and clay; nutrient recommendations; and recommendations for soil amendments.]

1.7	DELIVERY, STORAGE AND HANDLING

.1	Remove all equipment and materials off site each day unless on site storage is approved by Minister.

.2	Store tools, equipment and materials in a secure area when not in use during period of operation and at the completion of each scheduled task.

.3	Contractor shall be present on site to accept delivery of all equipment and/or material shipments.  Acceptance of delivery by Minister shall not constitute acceptance or responsibility for any of the materials or equipment.

1.8	EXAMINATION OF SITE

.1	Within ten days of commencement of contract, thoroughly examine the existing landscape conditions on site.

.2	Prepare a list of all plants and turf areas that are dead, unhealthy or damaged.  List other landscape features such as irrigation sprinkler heads, hard surfaces, furnishings and other items of maintenance that are deficient or damaged and require correction.  Submit current photos to support list of deficient items.

.3	Submit list and review with Minister for approval.  Failure to submit and review required list of existing conditions with Minister may result in Contractor being responsible for any required correction.

1.9	DAMAGE TO PROPERTY

.1	Contractor shall be responsible for all damages to Minister’s property, the personal property of all employees, staff and visitors and the property of adjacent land owners resulting from the actions of the Contractor, the contractor’s employees, subcontractors or representatives who provide service under this contract.

.2	Immediately report all damages to Minister.

.3	Repair, replace or restore all damaged property to its original condition or better as directed by Minister.  Damages shall be promptly corrected within seven (7) days, unless directed otherwise by Minister.  Contractor shall be responsible for all costs to correct damaged property.

.4	Scalping of turf, mechanical damage or injury to plants, improper plant pruning, and damages resulting from improper use of chemical pesticides and fertilizers will be considered damage.

2.	Products

2.1	FERTILIZER

.1	Synthetic Turf Fertilizer:  apply a complete, premium grade, granular fertilizer, containing minimum 50% of total nitrogen derived from a slow or controlled release nitrogen source, with all essential macronutrients plus 1%-2% iron and other micronutrients to maintain turf in a healthy, vigorous and green condition.  Other types of fertilizer are not acceptable for use on site unless approved by Minister.

.2	Do not use any "weed and feed" fertilizer.

.3	Plant Fertilizers:  apply premium grade fertilizer for plants and annuals in accordance with soil analysis (if applicable) or as directed by Minister.  Use only slow or controlled released fertilizers.

2.2	TOPSOIL AND PEATMOSS

.1	Imported Topsoil:  natural, fertile, shredded, screened agricultural soil capable of sustaining healthy growth.  Topsoil shall be loose and friable, free of subsoil, clay lumps, stones in excess of 20 mm, live plants, roots or any other deleterious material greater than 20 mm diameter.  Topsoil shall be free of litter, foreign matter and toxic materials harmful to plant growth.   Topsoil containing construction debris, sod clumps, quackgrass or other noxious weeds is not acceptable.  Supply of topsoil shall meet the following requirements:

.1	Minimum 6% organic matter.

.2	Acidity/alkalinity shall range from 5.9 pH to 7.0 pH.

.3	Electrical Conductivity (E.C.) - level of soluble salts shall not exceed 1.5 dS/m.

.4	Texture:  “Loam Topsoil” in accordance with Canadian System of Soil Classification.

.2	Sphagnum Peatmoss:  decomposed plants, fairly elastic and homogeneous, free of decomposed colloidal residue, wood, sulphur and iron.  Minimum of 80% organic matter by mass, pH value between 4.5 and 6.0.  Furnished in an air-dry state, packed in standard bags or bales showing name of manufacturer.

2.3	water

.1	Supply clean fresh water, water tanker, equipment, sprinklers, and labour as necessary in maintenance of plants and turf areas unless directed otherwise by Minister.

.2	Record quantity of water supplied and applied on site in maintenance log.

.3	Where available, Minister may allow use of a limited supply of water from building source at no cost to Contractor.

2.4	PEST CONTROL

SPEC NOTE:  Edit item of work.  Determine if the supply and application of pesticides to control pests are to be included in contract or if the service is to be paid as extra work in contract when required or deemed necessary by Minister.

.1	Chemical Pest Control:  supply and apply required chemical pesticides including herbicides, insecticides and fungicides, when Integrated Pest Management (IPM) practices and techniques are considered ineffective in controlling or suppressing pest populations on site.

[  OR  ]

.1	Extra Work - Chemical Pest Control:  when Integrated Pest Management (IPM) practices and techniques are considered ineffective in controlling or suppressing pest populations on site, the Contractor shall submit a cost estimate to supply and apply approved chemical pesticides that include herbicides, insecticides and fungicides.  Contractor’s cost estimate shall either be based on an hourly rate or lump sum as determined by Minister.  Service shall only be performed if approved by Minister.  Minister reserves the right to obtain pest control services from other contractors who specialize in providing these services.

.2	Submit the following information for Minister’s review and approval before applying any pesticide:

.1	Identification of specific pest(s) on site that requires control.

.2	Trade name of chemical pesticide and manufacturer’s instructions for use.

.3	Manufacturer’s material safety data sheets for each chemical pesticide.

.4	Name and credentials of licensed pesticide applicator(s).

.3	Pesticide Application Records:  pesticide application record books shall be completed by the certified licensed applicator in accordance with Alberta Environmental Protection and Enhancement Act.  Submit record books at completion of each pesticide application on site Provide information regarding target weed, insect or other pest, mode, type, and rates of application and results, including date, time, weather conditions and name of applicator.

2.5	PLANT PROTECTION MATERIALS

.1	Rodent, Animal and Sun Protection:

.1	Woven wire mesh:  galvanized woven wire strands, 1.2 mm wire diameter or suitable alternative with an opening of 12.5 mm x 12.5 mm, c/w fasteners.

.2	Plastic:  perforated spiral strip for horticultural use.

.3	Burlap:  clean, minimum 2.5 kg/m mass, 150 mm wide c/w twine fastener.

2.6	SNOW FENCING

SPEC NOTE:  Edit or delete item of work to suit site conditions.  If snow fencing is included in contract, the Minister must advise Contractor as to approximate locations on drawings or by addendum, prior to bid submittals.

.1	Snow Fencing:  standard type, 1.2 m height; [supplied by Contractor] [supplied by Minister].  Contractor shall supply all metal posts and other accessories as required for installation.

SPEC NOTE: info for extra work item- Snow Fencing:  supply and/or installation shall be considered as extra work in contract when requested by Minister.  Contractor shall submit a cost estimate as instructed by Minister that will either be based on supply and installation or on installation of snow fencing where fencing is supplied by Minister.  Cost estimate will, however, include for all required metal posts and other accessories as necessary to securely install snow fencing.  Minister reserves the right to obtain competitive cost estimates from other contractors to supply and/or install snow fencing.

# 2.7	MAINTENANCE SCHEDULE

.1	Schedule:  submit a legible and detailed maintenance schedule prior to commencement of maintenance services.  List all daily, weekly, and monthly maintenance services and other tasks to be performed.  Review schedule with Minister for approval.

2.8	ANNUAL AND PERENNIAL FLOWERS

SPEC NOTE:  Delete entire item if no annual plantings are required in contract.

.1	Flowering Plants:  supply and install all flowering plants for designated plant beds.  Provide a legible plan(s) showing proposed planting layout complete with plant quantity for each plant bed location for Minister’s review and approval.  Where applicable, provide plants according to list of species, variety or cultivar, and of quantity determined by Minister. All flowering plants and plantings to meet the following requirements:

.1	Flowering plants shall be healthy, dense and free of disease and pests.

.2	Plants with elongated stems, widely spaced leaves, soft or discoloured spots, root bound containers, pest and wilting damage are not acceptable.

.3	Layout and installation of flowering plants shall ensure that plants are spaced 150 to 200 mm on centre to achieve a full, complete and appealing appearance.  Select individual and larger growing plant species shall be spaced accordingly.

.4	Substitutions are unacceptable without prior approval of Minister.  Provide Minister with list of alternative plants only if specified flowering plants are unavailable or of unacceptable quality.  Provide list of growers contacted regarding availability.

.5	Provide annual plants in bud stage, just prior to first bloom, hardened off and ready for planting.

.6	Plants shall be supplied in the following minimum sized nursery containers for acceptance:  jumbo six pack, 10 cm pots and 15 cm pots.  Plants supplied in undersized or damaged containers are not acceptable.

.2	Contractor shall arrange for Minister’s inspection and approval of all flowering plants on site, prior to installation.

.3	Minister reserves the right to reject any flowering plant found to be unhealthy or unappealing prior to or after installation.  Contractor shall immediately remove from site all plants deemed unacceptable by Minister and install new healthy flowering plants within three days at no additional cost.

3.	Execution

3.1	GENERAL WORKMANSHIP

.1	Minister will be the sole assessor of the Contractor’s maintenance performance and workmanship.

.2	Schedule timing of operations to plant growth, weather conditions and site use.  Do each operation continuously and complete within reasonable time period.

.3	Do not perform work in any location or manner that may endanger the health and safety of the public.

.4	Collect and dispose of excess material and debris to approved municipal disposal site following collection.

.5	Coordinate maintenance practices with Minister.  When necessary, alter maintenance schedules to accommodate Minister's site activities.

.6	Contact Minister when specified maintenance requirements cannot be met for any reason.

.7	Submit name and contact number of company representative for immediate or emergency service when necessary.

.8	Keep a copy of contract specifications and applicable reference documents on site at all times for employee use and reference.

.9	Contractor’s principle owner and/or site supervisor must attend all site meetings called by Minister to review workmanship and performance.

.10	Promptly correct all maintenance deficiencies.  Deficient work or services shall be corrected within two days of Minister’s notification or as directed otherwise by Minister.

3.2	SPRING CLEAN-UP

SPEC NOTE:  Edit item to suit landscape conditions on site.  Only include spring clean-up services that are required on site.

.1	Complete spring clean-up by May 15th, weather permitting.  When completion date cannot be met, promptly advise Minister of the circumstances.

.2	Remove and dispose of protective coverings and mulch used for winter protection.

.3	Clean, sweep, collect and remove sand, rock chips, salt and other debris accumulated during winter months from all maintained turf and hard surface areas.  Re-sweep turf and hard surface areas until completely clean and acceptable to Minister.  Dispose of all collected debris to approved municipal disposal site.

.4	Remove snow fence, stakes and sand storage containers supplied by Minister and store as directed by Minister.  Winter protection materials supplied by Contractor shall be removed from site.

.5	Collect and remove from site all dead vegetation, leaves, litter, and other debris from turf areas.  Rake clean dead patches of grass and fungal growth in lawn areas resulting from snow mold, where existing.

.6	Clean all planting beds, raised planters, tree wells, hedges, gravel/rock beds and other landscaped areas of all plant debris, weeds, leaves, litter, and other undesirable foreign matter and plant growth.  Reinstall loose plant bed edging materials.  Remove all collected debris and materials from site.

.7	Loosen and lightly cultivate non-mulched planting soil without disturbing roots of permanent plantings.  Edge plant beds evenly to depth of 100 mm using a sharp spade to make an angled cut.

.8	Sweep and clean all hard surface areas on site including curbs and gutters along site roads and parking areas.  Hard surfaces adjacent to building entrances shall be power washed to remove soil, gum and other foreign debris to maintain clean and tidy site appearances.

.9	Lightly roll turf areas where grass has lifted due to frost action.  Repair damaged or deficient turf areas by spreading adequate topsoil and grass seed.

.10	Mechanized Power Sweep:  power sweep and wash all access and service roads on site, delivery/loading areas, parking lots, paved loading ramps, site entry and exits, and other hard surfaces on site.  Coordinate task of power sweeping with Minister to minimize conflicts with facility and site users.  Work shall be performed during non-regular working hours and may require multiple site visits to complete.  Complete power sweep by May 15th.

[.11	Extra Work - Organic Matter:  if instructed by Minister, provide a cost estimate to supply and spread approved organic matter (peat moss) over all non-mulched planting beds during spring to a minimum depth of 50 mm.  Cultivate soil to a depth of minimum 150 mm without damaging existing plants.  Rake soil smooth and level.  Remove excess soil from site.  Indicate quantity of organic matter supplied and spread in maintenance log.  Provide service listed in cost estimate upon approval by Minister.]

3.3	TURF MAINTENANCE

.1	Turf Aeration:

.1	Identify all sprinkler heads and other obstructions with flags before aerating.

.2	Use a vertical motion coring aerator with hollow tines that will penetrate the turf, extract and deposit soil cores.  Aeration cores must be of minimum 75 mm depth and spaced no further than 90 mm apart.  Ensure soil has adequate moisture before aerating.  Do not aerate dry soil.

.3	Aerate all lawn areas during early spring or fall.  Provide aeration during first year of contract and every second year following.

.4	Aerate in minimum two different directions.  Remaining soil cores shall be left on turf to break down unless directed otherwise by Minister.

.5	Promptly repeat turf aeration where coring depth and spacing are deemed deficient or inadequate by Minister.

.6	Compacted Soil Conditions:  turf areas subject to heavy use that results in compacted soil conditions shall be aerated every year in contract.

.2	Turf Dethatching:

.1	Identify all sprinkler heads and other obstructions with flags before dethatching.

.2	Use a vertical cutting mower or power rake to dethatch lawn areas in early spring.  Cross lawn areas two to three times in varying cross directions.

.3	Dethatching of turf areas shall commence during first year of contract and every second year following unless directed by Minister.  Collect thatch and remove from site.

.3	Topdressing and Reseeding:

.1	Topdress and reseed turf areas which show root growth failure, deterioration, bare or thin spots, or which have been damaged by any means or cause.

.2	Mow turf to an approximate height of 40 mm.  After mowing, rake thoroughly, removing loose and dead grass, stones and debris.

.3	Spread fertile topsoil to maximum thickness of 15 mm, filling in low areas and bare spots.  For severely damaged turf areas place sufficient topsoil and rake level with finish grade.

.4	Overseed areas with a seed mixture equivalent to existing grasses and approved by Minister.  Seed at minimum rate of 4 kg/100 m2.

.5	Rake seed into topsoil and lightly roll as necessary.

.6	Apply water to ensure penetration of 80 mm and at frequent intervals to maintain vigorous growth.

.4	Sod Replacement:

.1	Replace and repair all areas of existing turf that have been damaged by any means or cause.  Damages considered too small for sod replacement shall be repaired with topsoil and grass seed to Minister’s approval.

.2	Cut out and remove square or rectangular areas of dead, damaged and unhealthy turf using mechanical sod cutter and hand tools.  Replace with new healthy sod.

.3	Rake existing topsoil before installing new sod.  Add topsoil to fill uneven and low areas.

.4	Butt new sod tightly to adjacent existing sod.  Finish grade of new sod shall match adjacent undisturbed turf.  Topsoil open and exposed joints.

.5	Water to ensure penetration of 80 mm and at frequent intervals to maintain healthy growth.

.5	Fertilizing - General:

SPEC NOTE:  Edit turf fertilization requirements, quantity and applications to suit location and existing turf conditions.  Generally, three applications of turf fertilizer are not required on most sites that can be considered of a lower profile.  Delete seasonal applications when considered unnecessary.

.1	Apply granular turf fertilizer as directed by Minister or in accordance with soil analysis reports, if applicable.  Use only mechanical equipment to spread fertilizer.  Check calibration of spreader to ensure specified application rate is used.

.2	Spread 50% of fertilizer in one direction, then 50% at right angles.

.3	Synthetic Fertilizer:  apply the following granular turf fertilizer unless directed otherwise by Minister.  Submit fertilizer sample to Minister for verification.  Indicate total quantity of fertilizer applied on site in maintenance log.

.1	Spring Application:  [all regularly maintained turf areas].  [all zone 1 and 2 turf areas].  Apply [26-14-6] [20-10-15] [         ] slow release granular fertilizer or similar at rate of 3 kg/100 m2 by May 25th.

.2	Summer Application:  [all regularly maintained turf areas].  [all zone 1 and 2 turf areas].  Apply [24-5-11] [24-0-12] [        ] slow release granular fertilizer or similar at rate of 3 kg/100 m2 by July 15th.

.3	Autumn Application:  [all regularly maintained turf areas].  [all zone 1 and 2 turf areas].  Apply 12-3-18 [         ] slow release granular fertilizer or similar at rate of 2 kg/100 m2 by October 1st.

.4	Water:  apply water immediately after spreading fertilizer.  [Supply water, trucking and accessories and apply required water to all turf areas] [or] [use site irrigation system where applicable].  Alternatively, Contractor shall time fertilizer applications prior to natural rainfall that will activate the fertilizer and produce the desired response.  Ensure moisture penetration of 50 mm minimum.

.5	Advise Minister prior to any application of turf fertilizer.  Upon completion of service, provide documentation along with invoice to support type and quantity of turf fertilizer applied on site.

.6	Watering - Mowed Areas:

.1	Areas with underground irrigation systems:  coordinate operation of irrigation system with Minister.  Ensure irrigation system is set and adjusted to achieve optimum coverage and efficiency.

.2	Building Source of Water:  supply hoses, sprinkler equipment, other accessories and labour to provide adequate watering from building hose bibs.

[.3	Extra Work – Water Supply:  if requested by the Minister, provide a cost estimate to supply clean water, water truck, equipment, pumps, portable sprinklers, accessories and labour for the maintenance of turf areas.  Provide services listed in cost estimate upon approval by Minister.  Minister reserves the right to obtain competitive quotes from other contractors to perform the work and may not necessarily award to Contractor.]

.4	Water shall be applied during early morning.  Achieve a moisture depth of 50mm.

.7	Mowing - General:

NOTE:  Edit mowing requirements to suit contract.

.1	Mowing Height:  cut and maintain turf areas at 60 mm to 80 mm respective of the growing season.  During periods of active growth, turf shall be mowed at minimum required mowing height.  During hot dry conditions or slow growth periods, turf shall be mowed at increased or maximum heights to maintain turf health.

[  OR  ]

.1	Mowing Height – Zoned Turf Areas:  cut and maintain zoned turf areas to the following required heights respective of the growing season.  During periods of active growth, turf shall be mowed at minimum required mowing height.  During hot dry conditions or slow growth periods, turf shall be mowed at increased or maximum heights to maintain turf health.  Height of mower blades must be adjusted to achieve the required turf height in each turf zone.

.1	Zone 1:  mow turf at a height of 60 mm to 80 mm.

.2	Zone 2:  mow turf at a height of 75 mm to 90 mm.

.3	Zone 3:  mow native turf areas at a height of 125 mm to 150 mm.  Mowing shall be performed twice during the growing season; once by June 15th, and once by September 1st.  Remove excessive accumulations of grass clippings.

.2	Mowing Schedule:  mow regularly maintained turf areas on weekly intervals during periods of active growth and more frequently during accelerated growth periods to maintain turf at required height.  Turf shall be cut less frequently or when directed by Minister at increased heights during periods of hot dry seasonal climatic conditions or when turf growth is slow.  Mowing shall occur during early morning or late evening during periods of infrequent cuts.

.3	Turf mowing shall generally occur when “one-third” of grass blade can be removed during a single cutting to achieve required turf height.  Schedule to complete mowing in one continuous operation, weather permitting.  Mowing turf when insufficient growth has occurred or cutting turf shorter than required will be considered unacceptable.

.4	Mow turf areas only when dry.  Use mowers with sharp blades that will cut turf cleanly.  Turf mowed when wet or with dull blades that tears and leaves ragged leaf edges is unacceptable.  Minister may periodically inspect mower blades for acceptance.

.5	During periods of extended moisture and excessive turf growth increase mower blade height and pre-cut turf at an increased height.  Remove clippings.  After turf dries, lower blade height to original height and double cut by mowing lawn a second time to achieve required turf height.

.6	Remove all papers, rocks, animal waste, and other foreign material from turf areas before cutting grass.

.7	Remove clippings after each turf mowing.  Short and unnoticeable grass clippings may be left on lawns that are regularly mowed at desired heights.

.8	Change direction of cut with each mowing to avoid soil compaction and turf wear or ruts from mower wheels.  In the event that turf damage or ruts result, immediately repair all damaged turf.

.9	During each cutting operation, temporarily relocate movable site furnishings.  Replace to approximate original location after mowing is completed.

.10	Edging:  use a mechanical power edger with fixed steel blade to cut and provide neat, uniform, and cleanly defined edges along all sidewalks, concrete curbs, and other hard surfaces on site.  Do not use string line monofilament trimmers for edging.  Provide monthly edging services during June, July, August and September.  Remove all edging debris from site.

.11	Trimming:  trim grass areas as follows:

.1	trim grass along fences, walls, sign posts, structures, monuments and adjacent to other fixed objects with a mechanical trimmer.  Turf shall be trimmed to same height as general turf ensuring that no turf is scalped.

.2	use hand trimmers to trim grass adjacent to trees and other plants to prevent damage to tree trunks, plant stems and roots.  Do not use string line trimmers near plants.  Cut and neatly trim grass around irrigation sprinkler heads to provide maximum water coverage.  Neatly trim grass around valve boxes, manholes, valves and all other structures located within turf area.

.3	avoid scalping turf or damaging any plant when trimming.  Remove resulting plant debris from site.

.12	Clean all sidewalks, stairs, roads, parking lots, curbs and gutters, hard surfaces, building walls and other locations of all grass clippings after each mowing to maintain clean site appearances.

.13	Damages:  immediately repair or replace damaged turf, plants and other site features resulting from improper and negligent use of string line trimmers, mowers and other equipment.  Promptly advise Minister of all damages.

.14	Minister reserves the right to reduce payment for unacceptable, incomplete or unnecessary turf mowing, trimming, edging and clean-up.

3.4	TREE AND SHRUB MAINTENANCE

.1	Monitoring:

.1	Regularly monitor and visually inspect the health and care of all plants on site to ensure proper plant care is provided in accordance with specifications.

.2	Indicate results of each plant monitoring inspection in maintenance log.

.2	Trees and Plant Beds:

SPEC NOTE:  Edit item to suit landscape conditions on site.

.1	Maintain all plants and plant beds weekly, to ensure healthy and vigorous growing conditions and aesthetically clean and pleasing site appearances.

.2	Cultivate all non-mulched plant beds and tree wells in upper 40 mm of soil bi-weekly to maintain a loose friable soil free from perennial weeds and grass.  Ensure soil is not mounded around base of tree trunk.

.3	Remove litter, debris, rubbish, animal waste and foreign plant growth weekly.  Dispose of collected materials off-site.  Remove all rocks larger than 15 mm from planted areas.

.4	Remove and eliminate perennial grass and weeds from all planted beds and tree wells areas weekly.  Control weeds by hand-weeding, contact spray herbicide and selective use of pre-emergent herbicides.  Apply herbicides in accordance with manufacturer’s instructions and with Minister’s approval.  Verify that herbicide is appropriate for use with various plant materials.   Contractor shall be responsible for any damages incurred as a result of herbicide use.

.5	Re-install uneven or loose edging materials located along plant beds.

.6	Edge all plant beds evenly to depth of 100 mm monthly to maintain original line and shape.  Use a sharp spade to make clean and neat angled cuts.  Where plants have outgrown the original plant bed, enlarge the plant bed by edging and removing all turf to outside edge of plant growth.  Remove all resulting debris from site.

.7	Edge and maintain neat, clean and circular tree wells of loose friable soil each month or less where tree wells already exist.  Provide and maintain a neatly cut edge at dripline area on coniferous plants and ensure well area is kept clean and weed free.  Remove and eliminate grass adjacent to trees when necessary to prevent damage from turf maintenance equipment.  Do not damage or cut roots of plants when re-edging or cultivating soil.

[.8	Tree Grates:  remove tree grates each month and thoroughly clean the planted well area.  Collect, remove and eliminate all weeds, debris and rubbish.  Replace grates after completion.  Cut and resize tree grates when necessary to prevent girdling and other damage to tree trunks.]

.9	Rake, level and re-spread wood mulch to achieve a fresh appearance and to correct any disturbances, monthly.  Clean and remove all debris, litter, weeds, grass and other foreign matter from mulched areas weekly.  Remove all perennial weeds and grass as necessary.

.10	Place fertile topsoil to correct any deficient or low area in plant beds.

.11	Straighten all leaning or sagging plants.  Replant if necessary.

[.12	Maintain soil lips around outer edge of plant pit.  Level soil lips or remove excess soil from site when plant is established.]

.2	Soil Conditioning:

.1	Maintain correct soil conditions in plant beds to promote optimum growth and health for each plant.

[.2	Extra Work – Soil Amendments:  provide a cost estimate to supply, spread and mix soil amendments to improve the physical properties of existing soil in accordance with a soil analysis report.  Soil amendment services shall only proceed upon Minister’s approval.  Contractor shall indicate all corrective measures taken and document final soil condition results in maintenance log.  Applications of synthetic fertilizers for turf and planted areas shall not be considered as extra work in contract in regards to soil amendments.]

.3	Staking and Tree Protection:

.1	Install or keep required stakes and guy wires taut and plants plumb during maintenance period.  Repair guy wires when defective.  Do not allow trees to be girdled from improper installation and maintenance of guy wires.

.2	Remove existing support stakes and staking accessories on all self-supporting plants.

.3	Install and keep plant protection materials in proper repair and adjustment when required or directed by Minister.

.4	Pruning:

.1	Prune in accordance with proper practices and standards described in “Pruning in Alberta” and “ANSI A300” (where applicable).  Minister will be the "Sole Judge" for assessing all pruning operations.  Promptly correct all deficient work when directed by Minister.

.2	Prune to provide a natural branching structure and to encourage a healthy natural growth pattern.  Balled or boxed shrub forms are unacceptable.

.3	Pruning shall be performed by Certified Arborists or trained and knowledgeable individuals approved by Minister.  Submit credentials of each individual who will perform plant pruning services on site for approval.

.4	Use sharp pruning tools and equipment to prune plants without tearing and ripping plant tissue.  Sterilize pruning tools after completion of each plant cutting operation and after pruning diseased plants.

.5	Do not strip lower branches or excessively raise crown of trees.  Stub cuts are not acceptable.

.6	Shearing/Topping:  do not shear or top any shrub or tree except for hedging plants unless authorized by Minister.

.7	Trees:  prune and remove dead, diseased, and damaged branches.  Prune and eliminate crossing, rubbing and obstructing branches.  Remove existing stubs, suckers, and water sprout growth.  Maintain adequate branch clearance.  Ensure coniferous trees have one dominant central leader where feasible.  Pruning shall generally be limited to an approximate height of 4.0 m in contract.

.8	Shrubs:  prune shrubs to maintain a natural form and healthy looking appearance.  Rejuvenate older shrubs by removing mature stems and unproductive wood at ground level.  Thin and remove crowded, crossing and rubbing stems and branches.  Remove all dead, diseased, damaged and undesirable branches.  Clear all plant growth that has overgrown public sidewalks while maintaining a reasonably balanced appearance.  Pinch back new candle growth every spring on plants such as Mugo Pine.

.9	Hedge Plants:  where applicable, trim and shear hedges in late June and August.  Use sharp hedge pruning tools to maintain a neat, clean and attractive appearance at height established by Minister.  Cut and remove all dead and diseased stems at base.  Remove all foreign ornamental sapling growth including roots growing within the hedge plantings.  Hedge trimming shall be straight and even.

.10	Remove all pruned wood, cuttings, diseased limbs and branches, debris and excess material off site to approved disposal location.

.11	Replace improperly pruned plants if directed by Minister.  Replacement plant shall match existing in size.

.5	Plant Removal and Replacement:

.1	Promptly remove from site all dead, unhealthy and unappealing ornamental plants and small trees (75 mm and under), including roots.  Place fertile topsoil to fill former plant pits.  Obtain approval of Minister for required work and note all plant removals in maintenance log.

.2	Replace dead or unhealthy plants that occur due to Contractor neglect or deficient maintenance with identical nursery grown plants of similar size.  Minister shall determine which plants require replacement.

.6	Fertilization Requirements in Early Spring:

.1	Apply plant fertilizer as directed by Minister or in accordance with soil test analysis (if applicable).  Use controlled or slow release plant fertilizers only.  Notify Minister prior to commencement of fertilization applications.  Record all fertilization activities in maintenance log.

.2	Trees:  apply 10-6-4 or similar plant fertilizer to all trees by June 1st at rate of 18 g/25mm of tree caliper.  Use a deep root feeder in application of plant fertilizer and water to dripline area to ensure plants are thoroughly fertilized and watered.

.3	Alternatively, place 16-10-9 or similar fertilizer spikes in ground at rate of one spike per 25 mm of caliper per tree around dripline of tree.

.4	Plant Beds – Ornamental Plants:  spread 14-14-14 or similar granular fertilizer by June 1st at minimum rate of 4 kg/100 m2 into upper surface of all planting beds.  Lightly rake into soil where applicable and apply water.  Record all fertilization in maintenance log.

.5	Apply adequate water after fertilizing to ensure penetration of fertilizer into soil and roots.

.7	Watering of Plants:

.1	Monitoring:  regularly test and monitor soil moisture conditions and a plant’s need for water to ensure adequate health and survival.  Natural rainfall, site irrigation, plant maturity and specie shall be considered in determining amount and frequency of watering.  Regularly review plant watering needs with Minister.  Contractor shall be responsible for ensuring that adequate moisture is provided when necessary to maintain healthy plant growth and to ensure plant survival.

.2	Use moisture sensor devices to test and measure availability of moisture in plant soil areas throughout site.  Record data in maintenance log.

.3	Site Water Source:  where applicable or available, use site irrigation system and other building water sources for plant watering needs.  Contractor shall coordinate operation of irrigation systems, where applicable, with Minister.  Supply all necessary equipment, accessories and labour to provide watering services when using any existing hose bib on buildings.

.4	Contractor shall supply clean fresh water, equipment, methods of transportation, water tanker, hoses and sprinklers, attachments and other accessories, and labour to adequately and efficiently apply water to plants that require watering where other means of watering are inadequate or not available.

.5	Newly Planted Plant Material:  where applicable, Contractor shall provide weekly  deep root watering services, when necessary, for all newly installed plant materials (five years and less) to ensure proper health and survival.  Minister shall advise Contractor as to location of all newly installed plants on site.

.6	Plant Watering:  apply minimum 40 liters of water per 25mm of tree trunk diameter (measure at 300mm above ground level) when watering.  Apply water using a deep root feeder throughout tree dripline area.  Saturate root area of each ornamental plant to maintain an adequate moisture level for healthy growing conditions.  Record total quantity of water applied in maintenance log after each day that plant watering activities are performed.  Indicate quantity of plants watered each day and their approximate location in maintenance log.

.7	Supply clean water, water truck and all accessories as necessary to adequately water and maintain plants where existing water is not available or inadequate.

3.5	ANNUAL and PeRENNIAL FLOWER MAINTENANCE

SPEC NOTE:  Requirements of this maintenance item only apply where annual flowering plants are required by Minister.  Delete items regarding extra work if not required or applicable.  Edit or delete remaining items regarding annual plant bed preparation, plant installation and maintenance to suit landscape requirements on site.

[.1	Extra Work:  Provide cost estimate to Minister for removal of existing annual plant bed soil and placement of approved garden mix when requested.  Estimate to include cost to excavate and remove existing plant soil to a required depth and install new replacement garden soil mix in annual plant beds and planters to required depth.  Only existing planting areas selected by Minister are to be prepared.  Minister reserves the right to modify requirements for soil improvements and to obtain competitive cost estimates from other contractors to improve or correct annual plant bed soil.]

[.1	Planting Media - Annual Planting Beds:

.1	Premium garden mix consisting of approximately 50% screened fertile topsoil, 35% organic compost (peat moss and other approved organic matter) and 15% clean sharp sand.  Submit sample of garden mix to Minister for approval including information on source of supply.]

[.2	Replacement of Existing Annual Flowering Planting Soil

.1	Excavate and remove from site the existing top layer of planting soil to a depth of approximately [100 mm] [150 mm] [        ].  Ensure all foreign debris, rock chips, perennial weeds and grass are removed.  Obtain Minister’s approval of soil excavation.

.2	Place and spread approved garden mix planting soil over plant beds to a minimum depth of [100 mm] [150 mm] [        ].  Obtain a finish grade after settlement of approximately 50 mm above finish grade of adjacent turf or hard surface after settlement.

.3	Planting soil shall be thoroughly roto-tilled to a minimum depth of 200 mm.  Rake and level cultivated soil and remove all foreign debris.]

.2	Annual Plant Bed Spring Preparations:

.1	Thoroughly clean annual plant beds and planters of all foreign matter, litter, rock chips, gravel, weeds, grass and other foreign plant growth.

.2	Install approved garden soil mix or organic matter to correct any uneven and low areas.

.3	Roto-till planting soil to a minimum depth of 150 mm.  Hand cultivate small planters.

.4	Apply 8-12-6 granular fertilizer at rate of 4 kg/100 m2 and work into soil.  Rake soil level and lightly water.  Place additional soil mix as necessary where settlement occurs.

.5	Obtain Minister’s approval of plant bed/planter preparations before installing any annual flowering plants.  Complete preparation of planting areas by May 25th.

.3	Installation and Maintenance:

.1	Install flowering plants in accordance with approved planting layout only after planting areas have been approved by Minister.

.2	Space annual flowers 150 to 200 mm on centre to achieve a full, complete and appealing appearance.  Space larger growing plant species accordingly.  Complete installation by June 1st or when threat of frost has passed.

.3	Perennials:  divide crowded and overgrown perennial plants, if applicable, and replant during spring season where directed by Minister.  Thoroughly water all plants after replanting and every week thereafter until well established.

.4	Fertilizer:  apply 20-20-20 fertilizer to flowering plants every two weeks during the growing season.  Record all applications of fertilizer in maintenance log.

.5	Deadhead faded flowers each week to ensure continuous blooms.

.6	Lightly cultivate plant bed soil each week to maintain a loose friable soil free from perennial weeds and grass.  Do not damage flowering plants when cultivating or hand weeding.  Keep annual plant beds and planters free of all foreign plant growth.

.7	Regularly collect and remove all litter, debris and other foreign matter from plant beds and planters.  Keep plant beds and planters free of all foreign debris.

.8	Watering:  frequently and thoroughly hand water all flowering plants as necessary to maintain adequate moisture within root systems and for healthy vigorous growth.  Provide clean water, water truck and all accessories as necessary to adequately water plants.  Contractor will be expected to water flowering plants seven days a week when necessary.  Never allow planting soils to dry out.  Record all applications of water in maintenance log.

.9	Pest Control:  apply pesticides when necessary to control specific disease and insect infestations on plants.  Removal of weeds from plant beds and planters shall be ongoing each week.

.10	Promptly remove from site all dead, unhealthy and unappealing flowering plants resulting from deficient workmanship, maintenance or from other causes.  Immediately replace all unacceptable plants with new healthy flowering plants.

3.6	INTEGRATED PEST MANAGEMENT

.1	Integrated Pest Management (IPM):

.1	Minister supports the management and control of pests using IPM principles that utilizes regular monitoring to identify pests, considers various control options (biological, physical, cultural, mechanical and chemical) before implementing an effective, economical and environmentally acceptable solution to prevent and suppress pests.

.2	Use IPM principles to reduce or eliminate a reliance on chemical pesticides.

.2	Provide knowledgeable advise regarding the identification of pests on site, controls to be implemented in management of pests and assessing the outcome of treatment actions.  Keep Minister informed of all pest concerns on site and controls implemented in management of pests.  Record all information in maintenance log.

3.7	PESTS: WEED, INSECT AND DISEASE CONTROL

.1	Pest Monitoring:

.1	Pest Monitoring:  regularly monitor and visually inspect all plants, turf and other landscape areas to identify potential pest problems and determine appropriate pest controls.  Pest problems include insect, disease and weed infestations that pose a serious and on-going threat to plant life on site.

.2	Ensure proper, positive identification of infestations.

.3	Indicate results of monitoring inspections in maintenance log.  Review all pest concerns with Minister.  Record all actions taken to control pest problems in log.

.2	General Considerations:

.1	Use of chemical pesticides are restricted as Minister supports the use of IPM practices.  Advise Minister on whether IPM practices are practical in managing and controlling any existing pests on site or if chemical pesticides are necessary.

.2	Determine the susceptibility of plant species to pesticide damage before requesting use of chemical pesticides.  Request the Minister’s approval where chemical pesticides are deemed necessary in the management and control of pest infestations.

.3	Applications of pesticides shall be performed in accordance with Alberta Environment’s current legislation.  Provide Minister with three days advance notification of intent to apply chemical pesticides on site.

.4	Use equipment and containers free of harmful residues not related to specific control measures applicable to situation.

.5	Certified Applicator:  when pesticides are deemed necessary to control pests, the application of each pesticide on site shall be performed by a certified pesticide applicator.  Personnel assisting the certified applicator on site shall be thoroughly trained and knowledgeable in pesticide applications and use of all equipment in accordance with Alberta Environment’s Code of Practice for Pesticides.  Applicator shall maintain pesticide application record books and submit at completion of each pesticide application.

.6	Prepare and apply pesticide according to manufacturer's specifications.  Minimize drift at all times.  Erect signs to notify building occupants and the public regarding pesticide use on site.

.7	Timing:  pesticides shall be applied at times, which limit any possibility of contamination from climatic and other factors.  Monitor weather conditions to avoid making application prior to inclement weather to eliminate potential runoff from treated areas.  Confine all applications to outside of regular site operation hours to avoid contamination from drift and its effect on surroundings, occupants of nearby buildings and site users.

.8	Ineffective or improper applications of pesticide shall be immediately terminated and corrected by Contractor.  Additional application of pesticides shall be completed approximately two weeks after initial application is noted as visibly inadequate or deemed deficient by Minister.

.3	Pest Control:

SPEC NOTE:  Edit item of work.  Determine if the supply and application of pesticides to control pests are to be included in contract or if the service is to be paid as extra work in contract when required or deemed necessary by Minister.

.1	Chemical Pest Control:  supply and apply required chemical pesticides including herbicides, insecticides and fungicides, when Integrated Pest Management (IPM) practices and techniques are considered ineffective in controlling or suppressing pest populations on site.

[  OR  ]

[.1	Extra Work - Chemical Pest Control:  provide a cost estimate when Integrated Pest Management (IPM) practices and techniques are considered ineffective in controlling or suppressing pest populations on site, to supply and apply approved chemical pesticides that include herbicides, insecticides and fungicides.  Contractor’s cost estimate shall either be based on an hourly rate or lump sum as determined by Minister.  Service shall only be performed if approved by Minister.  Minister reserves the right to obtain pest control services from other contractors who specialize in providing these services.]

.2	Weeds:

.1	Provide weed control and eradication methods that are continuous and ongoing during active growth and establishment.  Ensure weed seed heads are removed before maturity.  Implement IPM practices and techniques that include cultivation and physical methods where practical before applying chemical pesticides.

.2	Completely eliminate and remove from site all noxious weeds in accordance with government regulations.

.3	Eliminate all weeds within hard landscaped surfaces on site.  Control shall be thorough and effective.

.3	Insects and Disease:  apply pesticides based on development stage of insects' life cycles to prevent loss or damage to plant material.  Monitor turf areas and plants and apply approved pesticides to control pest infestations if IPM practices and techniques are not effective.

.4	Monitor effectiveness of each pesticide application and promptly correct any inadequate or deficient application.

.5	Repair and pay for damage caused by application of herbicides.

.6	Do not use soil sterilants.

[.7	Rodents:]

[.1	Extra Work:  provide cost estimate to control burrowing rodents by trapping and/or eradication methods that are approved by Minister.  Service shall only proceed upon submittal of cost estimate and Minister’s approval.  Minister reserves the right to obtain competitive cost estimates from other contractors who specialize in these services.]

3.8	IRRIGATION SYSTEM MAINTENANCE

SPEC NOTE:  requirements of this maintenance item of work shall only apply where underground irrigation systems exist on site.  Minister reserves the right to obtain irrigation services under separate contract with other contractors who specialize in providing irrigation installation and maintenance services.  Delete or edit this item if not applicable to site or if underground irrigation system will be maintained by others.

[.1	Irrigation system on site shall be maintained by others under contract to Minister.]

[  OR  ]

[.1	Monitor irrigation system within site and correct for coverage, adjustment, clogging of lines and removal of obstacles that obstruct the spray.]

[.2	Regularly check irrigation systems and adjust and/or repair any sprinkler head causing excessive runoff or which throw moisture onto pedestrian walks and vehicular roadways.  Repair all leaking valves or defective valves immediately upon occurrence.]

[.3	Adjust controller in consideration of water requirements, plant community and adverse weather changes.  Watering cycles shall be set to cause least inconvenience to site users.]

[.4	Conduct autumn blow-out and spring start-up in accordance with manufacturer’s instructions.]

[.5	Repairs and service requirements must be performed by qualified irrigation personnel who are regularly engaged in irrigation installations and maintenance.  All replacement material and workmanship shall be equal or better than original.]

3.9	AUTUMN PREPARATION

SPEC NOTE:  Edit item to suit landscape conditions on site.  Only include services that are required on site.  If deep root watering services are not practical or feasible item should be deleted or modified to suit actual plant needs and conditions on site.

.1	Leaf Removal:  rake and vacuum fallen leaves weekly and remove from site to approved waste recycling depot.  Continue until leaves cease to fall.

.2	Clean all plant beds, planters, tree wells, mulched areas, and other landscaped areas on site weekly.  Keep catch basins and all curbs and gutters clean and free of all debris.  Remove all collected leaves and other organic debris to approved waste recycling depot.

.3	Remove all annuals within one week after first killing frost or when directed by Minister and dispose at approved waste recycling depot.  Deep cultivate plant beds and planters following annual plant removal.

.4	Cut back foliage of perennial plants within one week after killing frost.  Stake locations of cut perennials and apply organic mulch around plants for winter protection as necessary.  Thoroughly water all plants for winter.

.5	Ornamental grass shall remain intact during winter and trimmed back the following spring unless directed otherwise by Minister.

.6	Deep root water all plants (except where directed otherwise by Minister) between October 1st and 15th in preparation for winter.  Supply water, trucking and other necessary accessories to adequately apply water to plants.  Trees to receive minimum 40 liters of water per 25 mm of trunk diameter (measure at 300 mm above ground level).  Apply water throughout tree dripline area.  Saturate root area of all ornamental plants.  Record total quantity of water applied and location of plant watering activity in maintenance log after each day of watering activity.

.7	Install appropriate protective materials to protect plants from rodent, animal and sun damages.

.8	Sweep and clean all walkways and other hard surface areas weekly.  Keep curbs and gutters free of plant debris and litter.  Remove all collected debris and litter from site.

[.9	Mechanized Power Sweep:  power sweep all hard surfaces on site.  Coordinate task of power sweeping with Minister to minimize conflicts with facility and site users.  Work shall be performed during non-regular working hours and may require multiple site visits to complete.  Complete power sweep by September 30th.]

[.10	Erect snow fencing in selected locations, where necessary or directed by Minister.]

3.10	CLEANLINESS OF GROUNDS

SPEC NOTE:  Edit item to suit cleanliness requirements for site.

.1	Site grounds shall be kept in a clean and tidy condition.   Provide weekly clean-up services to ensure aesthetically pleasing and desirable site appearances are continually maintained.  Sweep, clean, collect and remove all debris, litter, rubbish and pests each week in maintenance of site grounds.

.2	Provide prompt service within [3 hours ] [      ] when directed by Minister to correct or complete clean-up services deemed inadequate or incomplete.

.3	Dispose of all collected litter, material and other debris off site to municipal disposal site following each clean-up activity.  Contractor shall pay all off-site disposal costs.  Do not dispose of any debris in Minister’s disposal bins or elsewhere on site.

.4	Empty all trash receptacles on a weekly basis or more often when necessary based on usage.  Supply heavy duty refuse bags and replace after each trash removal.

.5	Sweep and clean all building entrances/exits, stairs, walkways, along all concrete curbs and gutters, and from all other hard surface areas each week as required.  Hand scrap and/or pressure wash building entrance areas to remove gum, soil and foreign matter when necessary to maintain clean appearances.  Keep catch basins free of all accumulated debris and litter each week.

.6	Keep condition of site furnishings clean and safe for use.  When necessary, site furnishings shall be pressure washed to maintain clean and sanitary appearances.  [Regularly clean cigarette snuffers and other ashtray furnishings].

.7	Keep washed rock, gravel, and wood mulched surfaces clean and free of all debris, litter and foreign plant growth each week.

.8	Make weekly inspections for vandalism and damage.  Immediately report vandalism and damage to Minister and note in Maintenance Log.

.9	Record all cleaning services performed each week in Maintenance Log.

END OF SECTION