Section Cover Page

Section 32 99 90 2018-08-15 Restoration of Sitework

Use this Section to specify restoration of existing areas and sitework damaged or disturbed due to earthwork or other work of the Contract, back to their original condition.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Related Requirements

2.	Products

Not Used

3.	Execution

3.1	Restoration, Generally

3.2	Restoration of Landscaped Areas

3.3	Restoration of Concrete Paving, Curbs, and Gutters

3.4	Restoration of Asphalt Paving

3.5	Restoration of Gravel Surfacing

1.	General

1.1	RELATED Requirements

SPEC NOTE:  Where extensive restoration work is required, include cross-references to appropriate Sections specifying work in detail.

.1	Fill Materials:	Section 31 05 13.

.2	Granular Base:	Section 32 11 16.

.3	Asphalt Paving:	Section 32 12 16.

.4	Concrete Paving, Curbs and Gutters:	Section 32 13 13.

.5	Interlocking Concrete Paving Stones:	Section 32 14 13.

.6	Road and Parking Appurtenances:	Section 32 17 10.

.7	Chain Link Fencing:	Section 32 31 00.

.8	Topsoil Placement and Grading:	Section 32 91 19.

.9	Seeding:	Section 32 92 19.

.10	Sodding:	Section 32 92 23.

.11	Trees, Shrubs, and Ground Covers:	Section 32 93 00.

2.	Products

.1	Not Used.

3.	Execution

3.1	RESTORATION, GENERALLY

.1	Restore all existing areas and sitework damaged or disturbed due to earthwork or other work of this Contract, back to their original condition [and to finish grades indicated on Drawings].

SPEC NOTE:  For minor work with minimal restoration requirements, the above "performance" requirement will suffice.  Where restoration is more extensive, foregoing article may be supplemented with following "prescriptive" requirements.

3.2	RESTORATION OF LANDSCAPED AREAS

.1	Replace topsoil in accordance with Section 32 91 19.

.2	Restore grassed areas by [seeding in accordance with Section 32 92 19] [sodding in accordance with Section 32 92 23].

3.3	RESTORATION OF CONCRETE PAVING, CURBS AND GUTTERS

.1	Restore sidewalks, curbs and gutters in accordance with Section 32 13 13.

.2	Restore interlocking concrete paving stones in accordance with Section 32 14 13.

3.4	RESTORATION OF ASPHALT PAVING

.1	Compact fill material to a level [300 mm] [      ] below finished surface grade.

.2	Place [       ] fill material to level of underside of existing asphalt.

.3	Where edges of existing paving have become ragged, cut paving to form a straight line prior to placing new paving.

.4	Thoroughly clean edges of existing paving and coat with bituminous bonding agent prior to placing asphalt.

.5	Place asphalt in maximum 75 mm lifts.

.6	Compact new asphalt paving using a steel wheel roller with a minimum weight of 8 tonnes.

.7	Ensure finished grade of asphalt paving conforms to existing surface with no rises, depressions or ridges.

OR

SPEC NOTE:  If asphalt restoration is very extensive, delete above and specify asphalt paving using Section 32 12 16.

.1	Restore asphalt paving in accordance with Section 32 12 16.

3.5	RESTORATION OF GRAVEL SURFACING

.1	Replace disturbed gravel surfacing with [           ] fill material to thickness equalling that of existing gravel.

.2	Grade gravel to match existing elevations and surfaces.

.3	Compact gravel to 95% of Standard Proctor Maximum Dry Density.

END OF SECTION