| GRADING DESIGN ESTIMATE FORM |
| --- |
| ESTIMATE TYPE: | “ B “ |  | PROJECT: | SH 999:00 |  |
| FROM: | West of |  | TO: | East of |  |
|  | Km | 12.345 | To Km | 28.345 |  | LENGTH: | 16.000 Km |  |
| DESIGN DESIGNATION: | RAU 209-110 |  | SUBGRADE WIDTH: | 12.6 m |  |
| INITIATED BY: |  |  | NATURE OF PRIORITY: |  |  |
| DATE: |  |  |  |  |
|  | ITEM | UNIT | QUANITY | UNIT PRICE | ESTIMATED COST |  |
|  | Common Exc. | m3 | 113,000 | $1.90/m3 | $214,700.00 |  |
|  | Borrow Exc. | m3 | 390,000 | $2.00/m3 | $780,000.00 |  |
|  | B.T.S. Exc. | m3 | 40,000 | $1.00/m3 | $40,000.00 |  |
|  | Channel Exc. | m3 | 40,000 | $3.00/m3 | $120,000.00 |  |
|  | Rock Exc. | m3 |  |  |  |  |
|  | Com/Bor Truck Haul | m3 |  |  |  |  |
|  |  | Total Excavation: | 583,000 |  |  |  |
|  | Clearing | ha | 38 | $2500.00/ha | $95,000.00 |  |
|  | Fencing | km |  |  |  |  |
|  | Overhaul | m3 km | 150,000 | $0.75/m3km | $112,500.00 |  |
|  | Water | m3 |  |  |  |  |
|  |  |  |  | TOTAL ESTIMATED COST: | $1,362,200.00 |  |
|  |  |  |  |  | x 1.25 factor = | $1,702,750.00 |  |
|  | Right-of-Way |  |  |  |  |  |  |
|  | R/W: |  | ha @ |  | $/ha = |  |  | 10 % Contingencies | $170,275.00 |  |
|  | R/W: |  | ha @ |  | $/ha = |  |  | 18 % Engineering | $306,495.00 |  |
|  |  | Damages = |  |  | 4 % Materials | $68,110.00 |  |
|  |  | Total = |  |  | Right-of-Way |  |  |
|  |  |  |  |  | Borrow Agreements |  |  |
|  |  |  |  | Utilities | $30,000.00 |  |
|  |  |  | TOTAL FOR “GRADING ESTIMATE”: | $2,277,630.00 |  |
|  | Borrow Agreements |  |  |  |  |  |  |
|  | Borrow Pits: |  | ha @ |  | $/ha = |  |  |  |  |  |
|  | Backslopes: |  | ha @ |  | $/ha = |  |  |  |  |  |
|  |  | Damages = |  |  |  |  |  |
|  |  | Total = |  |  |  |  |  |
|  |  |  | - Subtract Right-of-Way |  |  |
|  |  |  | + Gravel Surfacing (Grading Only) | $40,800.00 |  |
|  |  |  | TOTAL FOR “PROGRAM ESTIMATE” | $2,318,430.00 |  |
|  |  |  | (Total CPMS Grading “B” Est.) |  |  |
|  | Estimate based on 20__ Dollars. | Prepared by: |  | Date: |  |  |
|  | REMARKS: | No work on bridge structures. R/W and borrow costs already in place. |  |
|  |  | Length of project may be changed. |  |
|  | COPY SUBMITTED TO PROGRAM ENGINEER: |  | 20 |  |  | Copy to: |  |  |

| PRIMARY HIGHWAY 99:00 |
| --- |
| SURFACING STRATEGY AND BASIC STRUCTURAL DESIGN |
| Type “B” Surfacing Estimate (Based on AT 2011 Regional unit prices) |
| Rehabilitation Overlay | Existing Width (m) | Final Width (m) |
| km 16.20 – km 25.135 | 9.0 | 11.8 |
| km 25.135 – km 33.000 | 9.7 | 14.1 |
| km 33.000 – km 34.20 | 9.4 | 14.1 |
| Item | From km | To km | Width (m) | Thickness (m) | tonnes/ km | Est. Tonnes/km | Length (km) | Est. tonnes | Unit Price ($/t) | Estimated Cost |
| Grade Widening Granular Base Course (Des. 2 Class 25) |  |  |  |  |  |  |  |  |  |  |
| km 16.20 – km 19.260 | 16.20 | 19.26 | 5.5 | 0.330 | 4191 | 4200 | 3.06 | 12852 |  |  |
| km 19.260 – km 25.135 | 19.26 | 25.14 | 5.5 | 0.330 | 4191 | 4200 | 5.88 | 24675 |  |  |
| km 25.135 – km 33.00 | 25.14 | 33.00 | 4.7 | 0.280 | 3066 | 3100 | 7.86 | 24366 |  |  |
| km 33.00 – km 34.20 | 33.00 | 34.20 | 5.0 | 0.280 | 3262 | 3300 | 1.20 | 3960 |  |  |
| Inter., ent., crossovers, etc |  |  |  |  |  |  |  | 6585 |  |  |
| Total tonnage (GBC – Des. 2 Cl. 25) |  |  |  |  |  | 72438 | $11.75 | $851,150 |
| Rehabilitation Overlay |  |  |  |  |  |  |  |  |  |  |
| Asphalt Concrete Pavement (Mix Type 2 – EPS) |  |  |  |  |  |  |  |  |  |  |
| km 16.20 – km 19.260 | 16.20 | 19.26 | 13.0 | 0.050 | 1515 | 1550 | 3.06 | 4743 |  |  |
| km 19.260 – km 25.135 | 19.26 | 25.14 | 13.0 | 0.100 | 3029 | 3050 | 5.88 | 17919 |  |  |
| km 25.135 – km 33.00 | 25.14 | 33.00 | 4.7 | 0.050 | 548 | 550 | 7.86 | 4323 |  |  |
| km 33.00 – km 34.20 | 33.00 | 34.20 | 5.0 | 0.050 | 583 | 600 | 1.20 | 720 |  |  |
| Inter., ent., crossovers, etc |  |  |  |  |  |  |  | 2770 |  |  |
| Total tonnage (ACP – Type 2) |  |  |  |  |  |  | 30475 | $35.50 | $1,081,870 |
| Asphalt Concrete Pavement (Mix Type 8 – EPS) |  |  |  |  |  |  |  |  |  |  |
| km 16.20 – km 19.260 | 16.20 | 19.26 | 13.0 | 0.020 | 606 | 650 | 3.06 | 1989 |  |  |
| Inter., ent., crossovers, etc |  |  |  |  |  |  |  | 199 |  |  |
| Total tonnage (ACP – Type 8) |  |  |  |  |  |  | 2188 | $39.00 | $85,328 |
| Mobilization (8%) |  |  |  |  |  |  |  |  |  | $161,468 |
| Sub-Total – Construction (contract) Costs |  |  |  |  |  | $2,179,817 |
| Contingency (5%) |  |  |  |  |  |  |  |  |  | $108,991 |
| Engineering (10%) |  |  |  |  |  |  |  |  |  | $228.881 |
| Estimated Total |  |  |  |  |  |  |  |  |  | $2,517,688 |
|  |  |  |  |  |  | “B” Estimate Total (to nearest $1000) | $2,518,000 |