| ALBERTA Transportation Technical Standards Branch | Date: Aug 31, 2011 |
| --- | --- |
| SURFACING ESTIMATE WORKSHEET | File: Hwy. 41:08 |
| Designed by: D.C. | Hwy. 545:02 |
| Reviewed by: M.J. | A.R. 154 |
|  | ASPHALT CONCRETE PAVEMENT - EPS |  |
| “Contractor’s Supply With Option” |
| PROJECT: | Hwy. 41:08 |
| LOCATION | N. of Hilda Access - N. of Jct Hwy. 545 |
|  | km 21.850 - km 39.229 = 17.379 km |
| SUBGRADE EXCAVATION | allow 400 m3 |
|  | Subgrade Excavation : 400 m3 X 16.80 $/m3 = $6,720 |
| GRANULAR FILL (Pit- Run) Des. 6 - 125 | Backfill : 200 m3 X 2.33 t/m3= | 470 t |  |
|  |  | 470 t |
|  | Granular Fill Des. 6: 500 t X 20.00 $/t = $10,000 |
| GRANULAR FILL Des. 2-25 | Backfill : 200 m3 X 2.33 t/m3= | 470 t |  |
|  |  | 470 t |
|  | Granular Fill Des. 2 : 500 t X 33.00 $/t = $16,500 |
| ASPHALT CONCRETE PAVEMENT End Product Spec. Mix Type M1/200-300A |
| ‘A’ km 21.850 to km 39.229 = 17.379 km X 1,400 t/km = | 24,330 t |
| CB6-2.3M34B : |  |
| [ 1600 m2 + ( 350 m X 0.125 m ) ] X 0.050 m X 2.33 t/m3 + 10% = | 210 t |
| Int. 381 : |  |
| [ 2200 m2 + ( 500 m X 0.125 m ) ] X 0.050 m X 2.33 t/m3 + 10% = | 290 t |
|  | 24,830 t |
| Asphalt Concrete Pavement - E.P.S. Mix Type M1/200-300A: 24,900 t X 65.00 $/t = $1,618,500 |
| ASPHALT CONCRETE PAVEMENT End Product Spec. Mix Type S1/200-300A |
| ‘A’ km 21.850 to km 39.229 = 17.379 km X 750 t/km = | 13,040 t |
| CB6-2.3M34B : |  |
| [ 1600 m2 + ( 350 m X 0.300 m ) ] X 0.020 m X 2.33 t/m3 + 10% = | 90 t |
| Int. 381 : |  |
| [ 2200 m2 + ( 500 m X 0.300 m ) ] X 0.020 m X 2.33 t/m3 + 10% = | 120 t |
|  | 13,250 t |
| Asphalt Concrete Pavement - E.P.S. Mix Type S1/200-300A: 13,300 t X 70.00 $/t = $931,000 |
| ROADWAY LINES - Supplying Paint & Painting Directional Dividing + 2 Edge |
| ‘A’ km 21.850 to km 39.229 = | 17.379 km |  |  |
|  | 17.379 km |  |
| Roadway Lines - Supplying Paint & Painting Directional Dividing + 2 Edge : 17.38 km X 715.00 $/km = $12,427 |
| ROADWAY LINES - Supplying Paint & Painting Lane Dividing Lines – Turnout |
| km 22.060 to km 22.380 = | 0.320 km |
|  | 0.320 km |  |
| Roadway Lines - Supplying Paint & Painting Lane Dividing Lines - Turnout : 0.32 km X 501.00 $/km = $161 |
| INTERSECTION LINES - Supplying Paint & Painting All Lines |  |
| Int # 381 |  |
| Intersection Lines – Supplying Paint & Painting All Lines : 1 unit X 251.00 $/unit = $251 |
| SUPPLY OF AGGREGATE - WITH OPTION |  |
| Granular Fill : | 1,000 t |  |  |
| ACP : | 38,200 t |  |  |
| TOTAL : | 39,200 t |  |  |
| Supply of Aggregate - With Option : 39,200 t X 2.50 $/t = $98,000 |
|  | MOBILIZATION (10 %) |  | $269,356 |
|  | SUB-TOTAL | $2,962,915 |
|  | CONSTRUCTION COST | $2,963,000 |
|  | CONTINGENCY (5 %) | $148,150 |
|  | ENGINEERING (10%) |  | $311,115 |
|  | TOTAL ESTIMATED COST | $3,422,000 |
|  | (to nearest $1000) |  |

| ALBERTA Transportation Technical Standards Branch | Date: Aug 31, 2011 |
| --- | --- |
| SURFACING ESTIMATE WORKSHEET | File: Hwy. 41:08 |
| Designed by: D.C. | Hwy. 545:02 |
| Reviewed by: M.J. | A.R. 154 |
|  | ASPHALT CONCRETE PAVEMENT – EPS |  |
| “Contractor’s Supply With Option” |
| PROJECT: | Hwy. 545:02 |
| LOCATION: | From Jct. Hwy. 41:08 to Saskatchewan Border |
|  | km 0.000 - km 6.511 = 6.511 |
| SUBGRADE EXCAVATION | allow 100 m3 |
|  | Subgrade Excavation : 100 m3 X 16.80 $/m3 = $1,680 |
| GRANULAR FILL (Pit-Run) Des. 6 - 125 | Backfill : 50 m3 X 2.33 t/m3 = | 120 t |  |
|  |  | 120 t |
|  | Gran. Fill Des. 6: 150 t X 20.00 $/t = $3,000 |
| GRANULAR FILL Des. 2 - 25 | Backfill : 50 m3 X 2.33 t/m3 = | 120 t |  |
|  |  | 120 t |
|  | Gran. Fill Des. 2: 150 t X33.00 $/t = $4,950 |
| ASPHALT CONCRETE PAVEMENT End Product Spec. Mix Type L1/200-300A |
| ‘B’ km 0.000 to km 6.511 = 6.511 X 1,950 t/km = | 12,700 t |  |  |
|  | 12,700 t |  |
| Asphalt Concrete Pavement - E.P.S. Mix Type L1/200-300A : 12,700 t X 68.00 $/t = $863,600 |
| ROADWAY LINES - Supplying Paint & Painting Directional Dividing + 2 Edge |
| ‘B’ km 0.000 to km 6.511 = | 6.511 km |  |  |
|  | 6.511 km |  |
| Roadway Lines - Supplying Paint & Painting Directional Dividing + 2 Edge 6.51 km X 715.00 $/km = $4,655 |
| SUPPLY OF AGGREGATE - WITH OPTION |  |
| Granular Fill : | 300 t |  |  |
| ACP : | 12,700 t |  |  |
| TOTAL : | 13,000 t |  |  |
| Supply of Aggregate - With Option : 13,000 t X 2.50 $/t = $32,500 |
|  | MOBILIZATION (10 %) | $91,039 |
|  | SUB-TOTAL | $1,001,424 |
|  | CONSTRUCTION COST | $1,002,000 |
|  | CONTINGENCY (5 %) | $50,100 |
|  | ENGINEERING (10 %) |  | $105,210 |
|  | TOTAL ESTIMATED COST |  | $1,157,000 |
|  | (to nearest $1000) |  |

| ALBERTA Transportation Technical Standards Branch | Date: Aug 31, 2011 |
| --- | --- |
| SURFACING ESTIMATE WORKSHEET | File: Hwy. 41:08 |
| Designed by: D.C. | Hwy. 545:02 |
| Reviewed by: M.J. | A.R. 154 |
|  | ASPHALT CONCRETE PAVEMENT – EPS |  |
| “Contractor’s Supply With Option” |
| PROJECT: | A.R. 154 |
| LOCATION: | From Jct. Hwy. 41:08 to E. of Hilda |
|  | km 0.000 - km 5.124 = 5.124 km |
| ASPHALT CONCRETE PAVEMENT End Product Spec. Mix Type L1/200-300A |
| ‘C’ km 0.000 to km 5.124 = 5.124 km X 1,050 t/km = | 5,380 t |  |
|  | 5,380 t |
| Asphalt Concrete Pavement - E.P.S. Mix Type L1/200-300A: 5,400 t X 68.00 $/t = $367,200 |
| ROADWAY LINES - Supplying Paint & Painting Directional Dividing + 2 Edge |
| ‘C’ km 0.030 to km 5.124 = | 5.09 km |  |  |
|  | 5.09 km |  |
| Roadway Lines – Supplying Paint & Painting Directional Dividing + 2 Edge: 5.09 km X 715.00 $/km = $3,640 |
| SUPPLY OF AGGREGATE - WITH OPTION |  |
| ACP : | 5,400 t |  |  |
| TOTAL : | 5,400 t |  |  |
| Supply of Aggregate - With Option : 5,400 t X 2.50 $/t = $13,500 |
|  | MOBILIZATION (10%) | $38,434 |
|  | SUB-TOTAL | $422,774 |
|  | CONSTRUCTION COST | $423,000 |
|  | CONTINGENCY (5%) | $21,150 |
|  | ENGINEERING (10%) | $44,415 |
|  | TOTAL ESTIMATED COST | $489,000 |
|  | (to nearest $1000) |  |